## Slide 1: Guest Lecture Stanford ME469: Multiphysics Coupling
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE

## Slide 2: Multiphysics Coupling: Outline
Examples of multiphysics coupling with emphasis on fluids, PMR, and CHT
Monolithic vs Operator Split
Details of PMR/Fluids Coupling
Details of PMR/Thermal Coupling
Details of Fluids/Thermal Coupling
Verification
Stability
Conclusions

## Slide 3: We Live in a Multiphysics World
Fluid/Structure coupling:
  Wind turbines
  Wing fluttering, etc.
Non-isothermal fluids/participating media radiation:
  Fires,
  Natural gas and coal combustion,
  Smelting, ethlyne production, etc.
Conjugate heat transfer:
  Object-in-fire
  Gas turbine fine cooling
Often times, we note a time and length scale disparity
  For example, consider heating a pan on a home burner
The coupling architect must generally choose between monolithic and split
For monolithic, the equations are provided, therefore, the challenge becomes managing a monolithic sytem solve, storage and code design
For operator split, there can be an “art” in determination of stable couplings due to Eignevalue spread

## Slide 4: Conjugate Heat Transfer Coupling
Convection Coef/Temp .
Common in engineering applications that require efficient heating or cooling of objects
Temperature
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
1 DOF/node
+ chemistry
Turbulent
Fluid Mechanics,
Combustion
15 dof/node
Thermal
Fluids
Tb
Turbulent pipe CHT
Tb

## Slide 5: Conjugate Heat Transfer Coupling, Equations
Favre-averaged static enthalpy equation:
Thermal heat conduction
Interface condition

## Slide 6: Fluid/CHT Coupling Verification
Unstructured heterogeneous mesh capability
Arbitrary geometric complexity
Multi-block domain variable transfer
Non-
conforming interface
Conforming interface
Linear (patch test)
Trigometric MMS

## Slide 7: Fluids/PMR Coupling
T, m, SRTE
Participating
Media
Radiation
n(n+2) DOF/node
VOLUME
Turbulent
Fluid Mechanics,
Combustion
15 dof/node
PMR
Fluids
Deflected reacting jet
Pool fire

## Slide 8: Fluids/PMR Coupling Equations
Favre-averaged static enthalpy equation:
Steady, non-scattering Radiative Transport Equation
Scalar Flux,
Divergence of radiative flux,
Quadrature

## Slide 9: PMR/Thermal Coupling
Irradiation
Temperature
Participating
Media
Radiation
n(n+2) DOF/node
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
1 DOF/node
+ chemistry
Thermal
PMR
ro, To = 0.1 m, 600K
r2, T2 = 0.075 m, 599.291K
ri, Ti = 0.03 m, 300K
r1, T1 = 0.05 m, 302.834K
PMR:Conduction through concentric spheres
O(1.8) with faceting,
O(2) without

## Slide 10: PMR/Thermal Coupling Equations
Steady, non-scattering Radiative Transport Equation
Irradiation (incoming),
Grey, diffuse boundary condition (given transmissivity, t, emissivity e, and reflectivity, r
With boundary condition,

## Slide 11: Conjugate Heat Transfer Stability
Compute amplification factor
Requiring:
CHT via flux transfer:
  Explicit RHS
  Unstable for certain time steps and material properties
CHT via convection coefficient:
  Implicit LHS
  Unconditionally stable
Consider a simple CHT problem
Simplified 1D geometry with 2 nodes for stability analysis of CHT

## Slide 12: Conjugate Heat Transfer Stability, In Practice
Transient heated laminar pipe in a 180 degree bend
  Water, Re = 2000, inflow T = 300
  Copper jacket, boundary – 350K

## Slide 13: Other Linearization Procedures
PMR and heat conduction radiative boundary condition:
PMR and fluids coupling, linearized divergence of the radiative flux,
In practice, such procedures enhance stability for the multi-physics coupling
In the case of Fluids/CHT, one could possibly monolitically couple the systems
In the case of Fluids/PMR, monolithic coupling is not practical as the intensity system is ~ N2, where N is generally O(8)

## Slide 14: Multiphysics Coupling: Conclusions
Multiphysics applications are abundant in engineering applications
Turbulent, reacting flow with PMR and CHT requires a wide range of length and time scale resolution
Monolithic approaches are ideal from a splitting perspective, however, can be prohibitively expensive when considering systems such as PMR
Linearization can augment time step stability and should be exploited when possible