## Slide 1
Stefan Domino, Ph.D.
Computational Thermal & Fluid Mechanics
Sandia National Laboratories SAND2019-15457 PE
An Evolution of a Mindset: A Historical Perspective on Sandia National Laboratories Fire Science Philosophy
Stanford ICME Seminar Series
January 30th, 2020 Stanford University

## Slide 2: Presentation Objectives
Pool Fire Heat Transfer Mechanisms
Physics Overview
Evolution from Quiescent, to Crossflow, to Whirling
Turbulence Modeling Choices
Solution Verification Concepts Demonstrated
Coupling and Discretization Overview
Conclusions
Interleaved Research Thrust Concepts:
  Fire Dynamics in Crossflow
  Automatic Structural Uncertainty Approaches
  Quality generalized unstructured numerics
  Extreme-scale computing
  Machine Learning for Wall-Modeled Large-Eddy Simulation (LES)

## Slide 3: To be Human is to Intuitively Understand the Dynamics of Fire
  Evidence of cooked food dates back ~two million years, Gowlett and Wrangham Azania: Archaeological Research in Africa, 2013
  The first example of controlled fire usage could date back ~one million years, Bowman et al., Science, 2009
  Widespread evidence of usage ~100,000 years ago
  Therefore, humans have an innate understanding of how fire sounds, feels, and behaves
10 meter outdoor fire (Nikos)
Fire feature soot plating
(Monterey, CA)
Intermittent wind gust
Luminaria (Santa Fe, NM)

## Slide 4: Heat Transfer Mechanisms: Abnormal/Thermal Environment (ATE)
object
  Characterized by a highly sooting, turbulent reacting flow with participating media radiation (PMR) and conjugate heat transfer (CHT) multi-physics coupling
  Liquid fuels, e.g., JP-8, are common due to its usage in transportation, however, propellants (point-Lagrangian/Eulerian) and composite (heterogeneous combustion) also encompass the ATE
Anderson Air Force B-2 Accident (2/2008)
[1]
[1] https://en.wikipedia.org/wiki/2008_Andersen_Air_Force_Base_B-2_accident
Propellant upward burn

## Slide 5: Grand Challenge: Vast Disparity in Time- and Length-Scales
Engineering Scale of Interest
Convective Transport
Heat Transfer in Weapon
Flames
Chemical Kinetics
Molecular Transport
Diffusive Transport
Soot
Products
Fuel Distribution
Convection
Molecular Radiation
Soot Radiation
Soot Growth
10-10
102
10-8
10-6
10-4
10-2
100
Length Scale, meters
Time Scale, seconds
10-12
10-9
10-6
10-3
100
103

## Slide 6: Evolution of a Mindset …. Quiescence
“There is no better, there is no more open door by which you can enter into the study of natural philosophy, than by considering the physical phenomena of a candle”
The Chemical History of a Candle, Michael Faraday (1791-1867)
Q:
O’Hern et al., JFM, 2005
Tieszen et al., C&F 2002
FLAME facility
ODF; Martins et al, 2005
“In the middle of the flame, where the wick is, there is this combustible vapor; on the outside of the flame is the air which we shall find necessary for the burning of the candle”
Ox
F

## Slide 7: Evolution of a Mindset: From Simple to Complex
  Peak radiative heat fluxes to engulfed objects is a function of fuel type, pool size, obstructions/accident geometry, and presence of crossflow
  As crossflow and geometric complexity of accident scenarios increase, SNL has found that transitioning from a Reynolds-Averaged Navier-Stokes (RANS) to a more predictive large-eddy simulation (LES) approach is required  HPC on Next-Gen platforms (NGP)
Quiescent; q”r
~ 100 kW/m2
Whirls
>> 200 kW/m2
RANS-based
LES-based
Cross-flow; q”r
~ 200 kW/m2

## Slide 8: Choice of Turbulence Modeling
  Direct Numerical Simulation (DNS), Large Eddy Simulation (LES) and Reynolds-Averaged Navier-Stokes (RANS) approaches define the computationally required time- and length scales
  Pool Fire Use-Case: large length and time scales challenge compute platforms
    1 cm resolution for a ten meter pool fire would require ~1 billion elements (only to a height of 1D)
    1 mm ~ 1 trillion elements (neglects bluff body requirements)
[1] https://sites.google.com/site/smokeisnojoke/lesrans2.jpg
Direct Numerical Simulation:
  Simulation captures all relevant length- and time-scales
  No turbulence modeling
  Very expensive; total cost ~Re3
Large Eddy Simulation
  Resolve the large-scale motion that contains most of the flow’s energy
  Model small scale based on scale- similarity
  Model = f(D)
Reynolds-Averaged Navier-Stokes
  Model the turbulence spectrum
  Empirical in nature
[1]

## Slide 9: Fires/Plumes in Quiescent Conditions: The classic Abnormal/Thermal Environment (circa 1990)
  Quiescent pool fires are, essentially, large-scale diffusion flames, i.e., mixing limited non-premixed combustion
  Several instabilities dominate, including Rayleigh/Taylor (bubble spike, heavy on light fluid) and Kelvin Helmholtz (velocity shear between two streams)
Time-averaged (inset transient)
Vorticity generation (baroclinic torque), Rayleigh Taylor (RT) and
Kelvin Helmholtz(KH) instabilities are present
[1] https://en.wikipedia.org/wiki/Kelvin–Helmholtz_instability
[1]
Notes: https://en.wikipedia.org/wiki/Kelvin–Helmholtz_instability: A KH instability on the planet Saturn, formed at the interaction of two bands of the planet's atmosphere

## Slide 10: Quiescent Fire/Plume Physics
  Fires, just as all buoyant plumes, in quiescent conditions “puff”
  In this application space, radiative heat transfer dominates
Evolution of a Puff Cycle (O’Hern et al., JFM, 2005)
Hydrogen, Tieszen et al., C&F, 2004
Helium, O’Hern et al., JFM, 2005
Helium DNS, Domino, (unpublished) 2016
Cetegen and Ahmed, C&F 1993