## Slide 1
Stefan Domino, Ph.D.
Computational Thermal & Fluid Mechanics
Sandia National Laboratories SAND2019-15457 PE
An Evolution of a Mindset: A Historical Perspective on Sandia National Laboratories Fire Science Philosophy
Stanford ICME Seminar Series
January 30th, 2020 Stanford University

## Slide 2: Low-Mach Turbulent Reacting Flow Equation Set
  Favre-averaged, variable-density, low-Mach equation set using large-eddy simulation (LES)
    Acoustics are filtered via the low-Mach derivation (Rehm and Baum, J. Research NBS, 1978; Paolucci, SAND, 1982)
Given filter:
Subgrid Stress (SGS):
Smagorinsky:
Ksgs:
WALE:
Closure:
LES Models:
mixture fraction-based flamelet combustion with generalized heat loss (multi-D table look-up)
Soot: Koo et al. (2018) from Moss and Askit (2007)

## Slide 3: Thermal Radiation Technique: Discrete Ordinate Method (DOM)
Radiative Transport Equation (RTE) approach attributes:
    Requires discretization, stabilization, quadrature set, Tg, ma, ms, etc.
    A meshed interior “volume”; Note: e =f(Dxn,N)
  Large set of sparse linear solves ~ 8N2 (Thurgood); N ~ 4
  Path forward: conservative Streamwise Upwind Control Volume (SUCV) stabilization motivated by SUPG Burns et al.., Ntl. Heat Trans Conf., 1995, provided by Domino, SAND, 2014
RTE with isotropic scattering
+
Definitions:
Ik = Intensity for ordinate k
skj = ordinate k for direction j
w = test function
N = quadrature set, e.g., 2, 4, 6, .., 12
5 meter JP-8 Pool Fire
temperature and absorption coeff
skj

## Slide 4: Thermal (heat conduction) and multi-physics coupling
  The quantity of interest is generally thermal response, T = f(t,xi), and incident radiative flux, H
Thermal Equation (simple):
Thermal interface coupling:
Fluids/PMR coupling:
Intensity coupling:
Supplemental:
From fluids:

## Slide 5: Three-Way Reacting Flow (Fire Mechanics) Coupling Description
Monolithic, i.e., fully coupled, approaches are intractable due to the size of (u, v, w, p, h, hr, Z, Ik T)T
Stable and accurate operator split methods are, therefore, sought
  See Domino et al., AIAA, 2007
Temperature
Irradiation
Participating
Media
Radiation DOM
SIERRA
Transfer
VOLUME
SURFACE
Δ
۰qr
Temperature, mg
RTE Src
Linearized
Temperature
Convection Coef.
Reference Temp
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
Turbulent
Fluid Mechanics,
Combustion

## Slide 6: Example of Multi-Physics Operator Split Methods
Compute amplification factor: Tn+1 = l Tn Require:
CHT via flux transfer:
  Unstable for certain Dt and material property ratios
CHT via convection coefficient:
  Unconditionally stable, however, Dt error
Simplified 1D geometry with 2 nodes for stability analysis of CHT
Tspec
inflow
outflow
Temperature
Convection Coef.
Reference Temp
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
Turbulent
Fluid Mechanics,
Combustion

## Slide 7: low-Mach Codes Featured
Nalu Philosophy:
  Open-source BSD-clause 3
https://github.com/NaluCFD
(soon)
Sierra/Fuego Philosophy:
  Government use license or Cooperative R&D Agreement (CRADA)

## Slide 8: Reality: Meshing time for complex applications remains a significant bottleneck!
Many applications of interest include complex geometries
low-Mach fluids users interested in high-quality simulation results tend towards hexahedral-based topologies (if possible)
However, if a scheme is “design-order” accurate, and low-dissipation, any topology may suffice
  Cast this in terms of efficiency (not unlike the active discussion on low- vs higher-order)
Sometimes, the penetration of a low-Mach fluids physics addition for a given analysis is high as the meshing can be prohibitively complex and time consuming, O(months)
Research Thrust: Establish numerical accuracy/stability on generalized unstructured mesh topologies and deploy this methodology to conform to a fast-meshing architype
  Likely tetrahedral-, hybrid, or Voronoi-based, see Bres et al., AIAA 2018-3302, 2018)
UUR Example: Vestas V27 225 kw
Hybrid low-order hex/tet/pyr/wedge
Sample of a somewhat
complex geometry

## Slide 9: A Review of a Typical V&V Workflow
Verify on nice Hexahedral-based elements
Validate on perfect meshes on a variety of canonical flows
Ret 395 plain-channel (Jofre, Domino, Iaccarino, Flow, Turb. & Comb., 2018)
Variable-density low-Mach MMS (Domino, CTRSP, 2016)

## Slide 10: Paradigm Shift: Verify and Deploy High-Quality Unstructured Numerical Methods (Research Thrust)
Verify on awful hybrid mesh element quality
Validate on non-ideal meshes on a variety of canonical flows
P1/P1
P1/P2
P2/P2
P2/P1

## Slide 11: Chosen Discretization: Control-Volume Finite Element Method (CVFEM)
A combination between the edge-based vertex-centered and FEM is the method known as Control Volume Finite Element (CVFEM)
A dual mesh is constructed to obtain flux and volume quadrature locations
As with FEM, a basis is defined:
dual-volume definition
Edge-based assembles Aj and Volk to edges and nodes, respectively
Integration-by-parts over test function w:
However, define a test function, w, as a piece-wise constant function (Heaviside) to be 1 inside the dual volume and 0 outside. Gradient is a Dirac-delta function:
Leading to:
Aj
Volk

## Slide 12: Control-Volume Finite Element Method Attributes
CVFEM can be viewed as Petrov-Galerkin method
The method can also be promoted in polynomial space, see Domino, CTRSP, 2014 as a first example of low-Mach fluids algorithm – or Domino, JCP, 2018
Research Thrust: Possible higher efficiency on NGP due to increased local work)
However, suitability of higher-order for LES is an open argument – especially when other errors/uncertainties exist
Spectral convergence
Dual-volume for promoted quad4
P=1 (left) and P=4 (right)
Helium plume (VR-density)
Rotating cube (Re 4000, RPM 3600)
P=1 (top) and P=2 (bottom)