## Slide 1
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4619 PE
Guest Lecture Stanford ME469: Nalu Overview

## Slide 2: Nalu Overview: Outline
Nalu Technology Origination: ASC
Beyond the 32-bit Limit
Supported Physics
Supported Numerics
Low- and High-order
Moving Mesh (Sliding and Overset)
Multiphysics:
  Fluid Structure Interaction
  Conjugate Heat Transfer (CHT)
  Participating Media Radiation
Examples
Conclusion

## Slide 3: Core Technology Provided to Nalu Origination: Advanced Simulation and Computing Sierra/Fuego
Use-case characterized by a highly sooting, turbulent, reacting flow with Participating Media Radiation (PMR), Conjugate Heat Transfer (CHT), and propellant multi-physics coupling
Complex geometry has driven a generalized, hybrid unstructured discretization approach supporting Hex8, Tet4, Wedge6, and Pyramid5 elements in addition to arbitrary promotion of Hex8 to Hex27, Hex64, etc.

## Slide 4: Goal: Beyond 32-bit Computing
Circa 2013, many scientific production codes were limited to 32-bit
Therefore, maximum simulation size for entities, e.g., node, edge, face, element, etc., was ~2.2 billion
Next Generation Platforms were advocated to overcome poor MPI scaling and power needs to support Exascale computing (1018 floating point operations/second)
  Platform architectures are not yet known
( )
Sierra Toolkit/Trilinos (open-source)
MPI+X parallelism
Support for new architectures
+ ASC IC
Investments

## Slide 5: Supported Physics

## Slide 6: Developed Open-Source BSD-clause 3 Distribution Policy
Philosophy: Open-source collaborations
https://github.com/NaluCFD
(soon)

## Slide 7: Nalu History
A time-history of the Nalu code base:
By CFD standards, this is a relatively new code base
Sierra/Nalu
SNL License
Github
Nalu
Open-source
BSD License (2014)
Active
academic partners
Github
Nalu-Wind
ECP ExaWind (2018)
Open-source: SNL, NREL, ORNL, UT joint copyright

## Slide 8: Supported Discretizations: CVFEM/FEM/EBVC
The core discretization used in the low Mach code base has been the Control Volume Finite Element Method, CVFEM
Finite Element Method and Edge-based Vertex-Centered, EBVC, are also supported

## Slide 9: Scientific Research Platform to Evaluate Higher-Order Methods on Next Generation Platforms
As the cost of parallel assembly increases, should we strive to perform more local work? Higher-order achieves this design-point (at the cost of a larger memory footprint)
Spectral convergence
Dual-volume
for promoted quad4
Flow-past rotating cube
Re~4000, RPM~3200
Same node count,
P=1 (top) P=2 (bot)

## Slide 10: Several Multi-physics Flow Examples
Impinging Jet DNS
Cylinder in cross flow
Whirling behavior
Helium plume (low-/high-order)
Heated backstep

## Slide 11: Evolution of a Mindset….. Modeling Whirling-like Flow
  Idealized chamber in which swirl is provided by selective wall placement in the experimental design
  Gap varied between 10, 20, and 40 cm
  Objective: Can the onset of swirl be predicted? What is the strength?
Volume rendered mixture fraction
SAND2019-7052 C
Notes: Fire whirls are complex phenomena that we are just understanding and, only recently, can model.
This is an example where we have engineered slots in walls that inspire vortical flow in the inner chamber. The plume accelerates upward and, therefore, entrains fluid. The slots provide a large-scale clockwise rotation.

## Slide 12: Unique Wind Energy Needs
Low-dissipation methods with suitable nonlinear stabilization operators to perform blade-resolved physics
Complex rotating blades, pitching blades, with possible yaw
Transition from low-order (near the blade) to higher-order (in the wake)
Vertical Axis Wind Turbine
(VAWT)
Horizontal Axis Wind Turbine
(HAWT)
Generalized, unstructured, hybrid low-order simulations shown

## Slide 13: Nalu Abstractions: Polymorphic and Input File-Driven
Domain
Time Integration
Realm B
Realm A
1 to many
boundary
algorithms
1 to many
Interior
algorithms
Transfer
1 to many
boundary
algorithms
1 to many
Interior
algorithms
Nonlinear Coupling
Operator-split multi-physics
Conjugate heat transfer coupling
Fluids Realm
Heat Conduction Realm
Realm specifications define the physics and desired boundary conditions
Pre-defined EquationSystems (segregated or monolithic)

## Slide 14: 30K View: Anatomy of a Nalu Input File:YAML-based
Simulation:
linear_solvers:
transfers:
realms:
- name: realm_heatCond
boundary_conditions:
- wall_boundary_condition: bc_exposed
solution_options:
initial_conditions:
material_properties:
equation_systems:
systems:
- HeatConduction:
output:
restart:
- name: realm_fluids
TimeIntegrators:
Specification of sparse Trilinos-based precond/solver
Data transfer for multi-physics coupling
Physics definitions
Time integration, e.g., BE, BDF2
YAML enforces strict spacing and ordering
https://www.democraticunderground.com/10021540110

## Slide 15: High-Level Elements of an Input File
systems:
- LowMachEOM:
name: myLowMach
- MixtureFraction:
name: myZ
initial_conditions:
- constant: ic_1
target_name: [block_1, …]
value:
pressure: 0
velocity: [0.5,0.0]
mixture_fraction: 0.0
material_properties:
target_name: block_1
specifications:
- name: density
type: constant
value: 1.0
- name: viscosity
type: constant
value: 1.8e-5
boundary_conditions:
- inflow_boundary_condition: bc_left_inflow
- wall_boundary_condition: bc_front_wall
- open_boundary_condition: bc_right_open
- symmetry_boundary_condition: bc_top
- nonconformal_boundary_condition: bc_nc
- inflow_boundary_condition: bc_left
target_name: surface_1
inflow_user_data:
velocity: [0.5,0.0,0.0]
mixture_fraction: 0.0
material_properties:
target_name: block_1
specifications:
- name: density
type: ideal_gas
- name: viscosity
type: polynomial
coefficient_declaration:
- wall_boundary_condition: bc_back
target_name: surface_7
wall_user_data:
user_function_name:
velocity: wind_energy
user_function_string_parameters:
velocity: [mmTop_ss7]
mixture_fraction: 1.0

## Slide 16: Test Case Input Files
  All input files are part of the Nalu regression test suite: Nalu/reg_test/test_files
  Mesh files are found under: Nalu/reg_test/mesh
    Formally, /mesh is a git submodule
  Test Cases Highlighted:
  Nalu/reg_tests/test_files/dgNonConformalThreeBlade
  Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
  Homework #1:
    https://github.com/spdomin/Present/tree/master/standformMe469/hwOne
Feel free to run any case that you feel looks interesting to you!
Note that the regression test suite is (mostly) focused on providing code coverage and may not represent “sane” physics-based choices
Resource: https://nalu.readthedocs.io/en/latest/source/theory/index.html

## Slide 17: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Physics
  Flow past rotating square blades (Re = 10,000)
Models
  Newtonian fluid (air) with constant properties
Boundary Conditions
  Inflow, open, symmetry, DG/CVFEM interface
>mpirun --np 4 /naluPath/naluX -i dgNonConformalThreeBlade.i &
Domino, JCP, 2018

## Slide 18: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Time Step Count: 7 Current Time: 0.0127268
dtN: 0.00266002 dtNm1: 0.00231306 gammas: 1.53488 -2.15 0.615116
Max Courant: 1.54421 Max Reynolds: 236.792 (realm_1)
Realm Nonlinear Iteration: 1/1
realm_1::advance_time_step()
NLI Name Linear Iter Linear Res NLinear Res Scaled NLR
--- ---- ----------- ---------- ----------- ----------
1/2 Equation System Iteration
1/1 myLowMach
MomentumEQS 4 1.27653e-07 0.000173716 1
ContinuityEQS 9 5.17721e-06 0.00618278 1
PNGradPEQS 19 4.2818e-09 2.78318e-06 1
PNGradUEQS 20 9.70201e-09 5.20951e-06 1
1/1 myZ
MixtureFractionEQS 5 1.31346e-09 6.84724e-06 1
PNGradZEQS 5 6.33586e-09 3.66957e-06 1
2/2 Equation System Iteration
1/1 myLowMach
MomentumEQS 5 8.33682e-10 2.23818e-06 0.0128842
Mass Balance Review:
Density accumulation: 0
Integrated inflow: -0.375
Integrated open: 0.3749998354138842
Total mass closure: -1.64586e-07
Mean System Norm: 0.0002458198407611864 7 0.0127268
gi for BDF2
UDt/Dx
r U L / m
nonlinear
iterations
equations
Review

## Slide 19: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Physics
  Uniformly emitting/absorbing participating media radiation (PMR) conjugate heat transfer (CHT) with buoyancy
Models
  Newtonian fluid (air): ideal gas
Boundary Conditions
  Wall, periodic
>mpirun --np 8 /naluPath/naluX -i fluidsPmrChtPeriodic.i &
Stark#, cond/rad
Sk = l m / s Ti3 ~ 0.4
Rayleigh#, tThermalDiff/ tConv
Ra = g b (Ti – To ) L / Pr a2 ~ 2e6

## Slide 20: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Monolithic, i.e., fully coupled, approaches are intractable due to the size of (u, v, w, p, h, hr, Z, Ik T)T
Stable and accurate operator split methods are, therefore, sought
  See Domino et al., AIAA, 2007
Temperature
Irradiation
Participating
Media
Radiation DOM
STK
Transfer
VOLUME
SURFACE
Δ
۰qr
Temperature, mg
RTE Src
Linearized
Temperature
Convection Coef.
Reference Temp
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
Turbulent
Fluid Mechanics,
Combustion

## Slide 21
Physics
  Laminar pipe flow (specified pressure drop)
Models
  Newtonian fluid (air): ideal gas
Boundary Conditions
  Wall, open (pressure specified)
Location: https://github.com/spdomin/Present/tree/master/stanfordMe469/hw/one
Specifications:
  Ret = 10
  Pipe diameter, D = 0.01 m
  Pipe Length, L = 0.2 m
  r = TBD
  m = TBD
  dp/dz = TBD
  Uc = TBD

## Slide 22: Nalu Overview: Conclusion
Nalu’s technology has its roots in the ASC Sierra/Fuego effort
Multi-physics capabilities are in development
Research platform for high-order low-Mach methods
Open-source collaboration model
Funded through ASC, ECP, A2e, ASCR, and LDRD