## Slide 1
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE
Stanford ME469: Common low-Mach Discretization Approaches

## Slide 2: Common low-Mach Discretization Approaches: Outline
The Concept of Meshing
Why Unstructured?
Unstructured Element Typoes
Finite Element Method (FEM)
Control-Volume Finite Element Method (CVFEM)
Edge-based Vertex-Centered (EBVC)
Cell-centered Finite Volume (FV)
Staggered arrangement
Conclusions

## Slide 3: Introducing a Mesh over Heart Domain, W
Notes: Geometry is:
Complex
Curved
Sharp

## Slide 4: Introducing a [Finite Difference] Mesh over Heart Domain, W
Notes: Geometry is:
Complex
Curved
Sharp
? What breaks..

## Slide 5: Introducing a [Finite Difference] Mesh over Heart Domain, W
Notes: Geometry is:
Complex
Curved
Sharp
? What breaks..
Not impossible: Chertock, et al., “A Second-Order Finite-Difference Method for Compressible Fluids in Domains with Moving Boundaries”, Commun. Comput. Phys., 2018

## Slide 6: Introducing a [Structured Mesh] over Heart Domain, W;
Notes: Geometry is:
Complex
Curved
Sharp

## Slide 7: Introducing a [Structured Mesh] over Heart Domain, W;
Notes: Geometry is:
Complex
Curved
Sharp
? What breaks..

## Slide 8: Introducing a [Structured Mesh] over Heart Domain, W;
Notes: Geometry is:
Complex
Curved
Sharp
? What breaks..

## Slide 9: Structured vs Unstructured
Many times, the canonical flows of interest are in simplified geometries that allow for cartesian meshes – with “stair-stepping”
Ret 395 plane-channel (Jofre, Domino, Iaccarino, 2018)
https://www.itascainternational.com/software/introduction-to-meshing
Often times, not!
RANS-based backward facing step (Domino, 2012)

## Slide 10: In Fairness…. The Carbon-Capture Multidisciplinary Simulation Center
http://ccmsc.utah.edu/about.html
15MW coal-fired boiler volume rendered image of large (90 mm) particles
Staggered schemes have been demonstrated to support complex applications
Cut-cells and embedded approaches help

## Slide 11: Introducing a Mesh over Heart Domain, W
Elements of size 4 (Quad4) or 3 (Tri3) have been introduced
Exterior domain is faceted
Non-conformal interface between the Tri3 and Quad4 block
Two types of connectivity have been presented: node:element and element:face:element
Two types of integration: We vs Wcv

## Slide 12: Introducing a Mesh over Heart Domain, W
Elements of size 4 (Quad4) or 3 (Tri3) have been introduced
Exterior domain is faceted
Non-conformal interface between the Tri3 and Quad4 block
Two types of connectivity have been presented: node:element and element:face:element
Two types of integration: We vs Wcv

## Slide 13: Data Structure Ramifications
A bit more complicated….
Element and associated data structures are indexed directly via ith and jth location, e.g., velocity_x(i,j), over the range: velocity_x(0:nX,0:nY)
Neighbors are directly indexed, e.g,, “north” neighbor of (i,j) is (i,j+1)
Element and associated data structures are indexed indirectly via a data structure, e.g., velocity_x(k), ober the range: velocity_x(0:nElem)
Neighbors of (k) are obtained via a relationship mapping obtained, e.g.,
std::vector<int> neighbor_elems
= elem_relationship(k);

## Slide 14: Integration Over the Domain
Consider a simple model equation with the heart domain in mind:
Integrating over the domain, W:
Without loss of generality, let us define a set of subdomains, Wk:
Where Fj is a flux and S is a source term
Note: Often the formality of Sk and Wk is dropped and is implied over the integration

## Slide 15: Mesh-based Methods Basic Concept: Sub-divide domain into Finite Elements and Numerically Integrate
Define basis within the domain:
While restricting to a Lagrange nodal basis,

## Slide 16: Reality: Meshing time for complex applications remains a significant bottleneck!
Many applications of interest contain complex geometries
low-Mach fluids users interested in high-quality simulation results tend towards hexahedral-based topologies (if possible)
However, if a scheme is “design-order” accurate, any topology may suffice as it is simply a matter of mesh size and efficiency – not unlike the active discussion on low- vs higher-order
Sometimes, the penetration of a low-Mach fluids physics addition in common analysis is high as the meshing can be prohibitively complex
UUR Example: Vestas V27 225 kw hybrid low-order hex/tet/pyr/wedge
Very complex world – stair-stepped!

## Slide 17: Examples of Various Topologies
Hex8
Tet4
Pyramid5
Wedge6
Arbitrary
Higher-order promoted elements (Hex27, Tet10, Wedge16, Hex64, etc.)

## Slide 18: Fundamentals of Discretization (Review)
Given a partial differential equation (PDE) and associated volumetric form:
Applying Gauss Divergence provides the standard finite volume form:
We can also multiple PDE by an arbitrary test function, w, and integrate over a volume,
Next, integrate by parts and apply
Gauss-Divergence. Note, that test function must be differentiable – shown here, at least once..
Sometimes, one notes T as Th - the trial space on given mesh size, h

## Slide 19: The Finite Element Method (FEM)
Consider the example in which the finite element method (FEM) is employed
Define an underlying nodal basis with the element:
Gaussian Quadrature is used
  using a -1:1 range, +/- sqrt(3)/3
Consider a simple heat conduction model PDE,
Integrate using a test function,
Integration-by-parts (with G-D) provides:
Iterate element quadrature points
Note that N can be arbitrary in order (shown here for a linear)

## Slide 20: The Hybrid Control-Volume Finite Element Method (CVFEM)
A combination between a vertex-centered finite volume and FEM is the method known as Control Volume Finite Element
A dual mesh is constructed to obtain flux and volume quadrature locations
As with FEM, a basis is defined:
Dual-volume definition
Integration-by-parts over test function w:
However, define a test function, w, as a piece-wise constant function (Heaviside) to be 1 inside the dual volume and 0 outside. Gradient is a Dirac-delta function:
Leading to:

## Slide 21: Control-Volume Finite Element Method Attributes
The CVFEM method, therefore, is a finite volume scheme that is locally conservative, i.e., momentum leaving one dual volume face enters the adjacent dual volume
However, the diffusion operator, like its FEM counterpart is absent of any error due to non-orthogonality
Suffers on high-aspect ratio meshes in presence of high gradients: sqrt(3)
Since the test-function, w, is different from the underlying basis representation, this method can be considered a Petrov-Galerkin method
The method can also be promoted in polynomial space (first fluids: Domino, 2014)
Spectral convergence
Dual-volume for promoted quad4
P=1 (left) and P=4 (right)
Helium plume (VR-density)

## Slide 22: Dual Volume Definitions for Hybrid Meshes
Domino, et. al, “An assessment of atypical mesh topologies for low-Mach large-eddy simulation” 2019

## Slide 23: Equal Order Interpolation Edge-Based Vertex-Centered (EBVC) Finite Volume
Same grad-op as CC:
Iterate nodes for volume contributions
Iterate edges for surface flux contribution
All primitives are collocated at the vertices of the elements with equal-order interpolation
A dual mesh is constructed to obtain flux and volume quadrature locations
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
Surface quadrature point (area summed to edge)
Volume quadrature point (sub-vol summed to node)
nj
Dual-volume definition
Edge-based stencil
TL
TR

## Slide 24: Equal Order Interpolation Edge-Based Vertex-Centered (EBVC) Finite Volume
Same grad-op as CC:
Iterate nodes for volume contributions
Iterate edges for surface flux contribution
All primitives are collocated at the vertices of the elements with equal-order interpolation
A dual mesh is constructed to obtain flux and volume quadrature locations
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
Surface quadrature point (area summed to edge)
Volume quadrature point (sub-vol summed to node)
nj
Dual-volume definition
Edge-based stencil
TL
TR

## Slide 25: Equal Order Interpolation Edge-Based Vertex-Centered (EBVC) Finite Volume
Same grad-op as CC:
Iterate nodes for volume contributions
Iterate edges for surface flux contribution
All primitives are collocated at the vertices of the elements with equal-order interpolation
A dual mesh is constructed to obtain flux and volume quadrature locations
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
Surface quadrature point (area summed to edge)
Volume quadrature point (sub-vol summed to node)
nj
Dual-volume definition
Edge-based stencil
TL
TR
Area vector
Dual nodal volume

## Slide 26: Equal-Order Interpolation Cell-Centered (CC) Finite Volume
Consider a simple heat conduction model PDE,
Integrate over a control volume and use Gauss-Divergence,
Iterate element cell-centers for volume contributions (time/source)
Iterate element faces for surface flux contribution
All primitives are collocated at the cell-center of the element with equal-order interpolation
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
TL
TR
Surface
quadrature point
with:
nj

## Slide 27: Typical Failings for Two-State Discretization Methods
With two points, only a linear basis can be used.
Therefore, unstructured CC and EBVC are limited to second-order spatial accuracy
Non-orthogonality is problematic for gradient-operator
Above, GjT is a projected nodal gradient at the cell-center, or vertex center:
Non-orthogonality is simply defined as the mis-alignment of the distance vector between the two ”L” and “R” states and the surface normal
Both edge- and cell centered-based schemes show degraded accuracy on typical production meshes
Several non-orthogonality approaches are available, for the best source, see Jasak
  Jasak, “Error analysis and error estimation for the finite volume method with applications to fluid flow”, Imperial College Dissertation, 1996
One Significant Advantage: Monotonicity preserving on high-aspect ratio meshes…
nj
Dxj
With area vector defined by:

## Slide 28: Classic Staggered Finite Volume
Velocity degree-of-freedom is staggered relative to pressure and other primitives, e.g., enthalpy, mixture fraction, etc.
Stencil for CC-quantities
Stencil for x-velocity
Stencil for y-velocity
PN
PS

## Slide 29: Attributes of a Staggered Scheme
By design, non-orthogonality is absent, however, complex geometry will be stair-stepped
From a fluids perspective, the operators are ideal, i.e., pressure gradient for momentum is compact, e.g., (PE – PW)Dx-1
  As will be seen in future lecture topics, the skew-adjoint nature of the Divergence operator, D, and Gradient operator, G, allows for a Laplace operator, L = DG
Can be extended to higher-order
Frequently, meshing complex geometries can be extremely difficult (consider our V27 example)

## Slide 30: An Informal Survey….
Cell-Centered: (Sometimes generalized Polyhedra)
  Ansys Fluent, OpenFOAM (FireFOAM, NavyFOAM), CD-Adapco (Star-CCM), Soleil-X (Stanford)
EBVC: (Most typical in the acoustically compressible space)
  SU2, FUN3D, CHAD, Nalu-Wind (production), Nalu (option to explore discretizations)
CVFEM
  Fluent (originally!), CFX-TASC-FLOW, Sierra Fuego (SNL), Nalu
FEM
  FIDAP, COMSOL, EDDY (NASA), AcuSim, PHASTA
Staggered
  Arches (Utah)

## Slide 31: An Informal Survey….
Cell-Centered: (Sometimes generalized Polyhedra)
  Ansys Fluent, OpenFOAM (FireFOAM, NavyFOAM), CD-Adapco (Star-CCM), Soleil-X (Stanforf)
EBVC: (Most typical in the acoustically compressible space)
  SU2, FUN3D, CHAD, Nalu-Wind (production), Nalu (option to explore discretizations)
CVFEM
  Fluent (originally!), CFX-TASC-FLOW, Sierra Fuego (SNL), Nalu
FEM
  FIDAP, COMSOL, EDDY (NASA), AcuSim, PHASTA
Staggered
  Arches (Utah)
Common Water-Cooler CFD Arguments:
Structured vs. Un-structured
FEM vs. Finite Volume
Node-centered vs. Cell-centered
Monolithic vs. Operator Split
Compressible vs. (acoustically) Incompressible
Explicit vs. Implicit

## Slide 32: An Informal Survey….
Cell-Centered: (Sometimes generalized Polyhedra)
  Ansys Fluent, OpenFOAM (FireFOAM, NavyFOAM), CD-Adapco (Star-CCM), Soleil-X (Stanforf)
EBVC: (Most typical in the acoustically compressible space)
  SU2, FUN3D, CHAD, Nalu-Wind (production), Nalu (option to explore discretizations)
CVFEM
  Fluent (originally!), CFX-TASC-FLOW, Sierra Fuego (SNL), Nalu
FEM
  FIDAP, COMSOL, EDDY (NASA), AcuSim, PHASTA
Staggered
  Arches (Utah)
Common Water-Cooler CFD Arguments:
Structured vs. Un-structured
FEM and Finite Volume
Node-centered vs. Cell-centered
Monolithic and Operator Split
Compressible vs. (acoustically) Incompressible
Explicit and Implicit

## Slide 33: Hybrid Meshes, Even for LES!
Hybrid mesh study based on Ham and Iaccarino, CTR Annual Brief, 2006, found that simulations were extremely sensitive to mesh topology
  Non-symmetric time mean flow found for cell-centered; better for the CTR node-centered formulation
Native CVFEM and EBVC are both symmetric in mean quantities
B
T
Domino, et. al, “The suitability of hybrid meshes for low-Mach large-eddy simulation” Stanford CTR Summer Program, 2018

## Slide 34: Recent Generalized Unstructured Findings
Domino, et. al, “An assessment of atypical mesh topologies for low-Mach large-eddy simulation” 2019

## Slide 35: A Note on Parallelism… Vertex-based
P1
P0
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
Sierra Toolkit/Standard Ownership rules: Mesh object (nodes, edges, faces, elements) owned by lower-rank. For example:
P0 locally owns E1 and nodes 1, 2, 4, and 5
P1 locally owns E2, E3, and E4 and nodes 3, 6, 7, 8, and 9
P0 and P1 share nodes 2, 4, and 5
Desired Control-Volume Finite Element (CVFEM) Operation:
“nodal volume” assemble for node 5 via iteration of each 1cmx1cm element. Desired nodal volume for node 5 = 1 cm2 exactly the same on both parallel ranks
Options:
1. Iterate over locally owned elements and locally accumulate nodal volume field followed by a parallel sum and copy owned to shared.
2. Ghost element E2, E3, and E4 to P0 and E1 to P1 (along with coordinates) and iterate locally owned and ghosted elements. Locally accumulate nodal volume field followed by a copy owned to shared.
edge 1
edge 2
face 1

## Slide 36: A Note on Parallelism… Vertex-based
P1
P0
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
¼
¼
¼
¼
Sierra Toolkit/Standard Ownership rules: Mesh object (nodes, edges, faces, elements) owned by lower-rank. For example:
P0 locally owns E1 and nodes 1, 2, 4, and 5
P1 locally owns E2, E3, and E4 and nodes 3, 6, 7, 8, and 9
P0 and P1 share nodes 2, 4, and 5
Desired Control-Volume Finite Element (CVFEM) Operation:
“nodal volume” assemble for node 5 via iteration of each 1cmx1cm element. Desired nodal volume for node 5 = 1 cm2 exactly the same on both parallel ranks
Options:
1. Iterate over locally owned elements and locally accumulate nodal volume field followed by a parallel sum and copy owned to shared.
2. Ghost element E2, E3, and E4 to P0 and E1 to P1 (along with coordinates) and iterate locally owned and ghosted elements. Locally accumulate nodal volume field followed by a copy owned to shared.
edge 1
edge 2
face 1

## Slide 37: A Note on Parallelism… Aura-based; View from P0
P1
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
Ghost P1 -> P0
P0

## Slide 38: A Note on Parallelism… Aura-based; View from P1
P0
P1
1
2
3
4
5
6
7
8
9
E1
E2
E3
E4
Ghost P0 -> P1

## Slide 39: Common low-Mach Discretization Approaches: Conclusions
Two-state methods, e.g., cell-centered and EBVC are attractive due to simplicity, however, suffer from non-orthogonality issues in the diffusion operator
Generally, CC or EBVC is 2x faster on a given mesh size
  Less accurate/stable on generalized unstructured mesh topologies
  Better diffusion operator on high-aspect ratio meshes
  Simple, single topology (virtual-, or full-edge)
FEM provides a machinery to provide accurate discretizations on non-ideal meshes, however, the same diffusion operator suffers on high-aspect ratio meshes
CVFEM is a hybrid method that contains the likeable attributes of both FV and FEM (same high-aspect ratio diffusion operator finding)
Staggered arrangement is well suited for a class of fluid mechanics applications where low-order or simple geometries are found
Examples for time/source/advection and diffusion provided for EBVC, CVFEM, and FEM
Recall that Nalu iterates over locally-owned mesh objects as apposed to local+ghosted
  This is a choice; however, the STK infrastructure allows for both approaches
  Test yourself on a dual nodal volume assembly?

## Slide 40
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE
Stanford ME469: Common low-Mach Discretization Approaches: EBVC

## Slide 41: Model Passive Scalar Transport
Time/Src/Advection/Diffusion equation for scalar f
Here, w is the weight function, or an arbitrary function that is differentiable - at least once
  Any ideas why? What are the properties of the above PDE?
In this example, let density, velocity, and diffusive flux coefficient be prescribed
This equation, with a prescribed velocity, can be used to model trace species contaminant transport, smoke, etc.
The above equation is termed a weighted-residual statement of the original PDE
Thus far, it is exact

## Slide 42: Model Passive Scalar Transport; Heaviside Test Function
Time/Src/Advection/Diffusion equation for scalar f
Recall, the CVFEM and EBVC test function meets our requirement in that it is differentiable once
This definition also allows us to view such methods as Petrov-Galerkin schemes

## Slide 43: Model Passive Scalar Transport: Fully Implicit
Time/Src/Advection/Diffusion equation for scalar f

## Slide 44: Model Passive Scalar Transport: Fully Implicit
Time/Src/Advection/Diffusion equation for scalar f

## Slide 45: Model Passive Scalar Transport: Coupling
Our fully coupled implicit system consists of: continuity, momentum, and mixture fraction
do while (!converged) {
}
For a given
time step:
{
Left-hand-side (LHS) or Jacobian is simplified for the passive scalar system
ADx = b – Ax*=-res

## Slide 46: Model Passive Scalar Transport: Coupling
Our fully coupled implicit system consists of: continuity, momentum, and mixture fraction; shown below in “residual form”
do while (!converged) {
}
For a given
time step:
{
Left-hand-side (LHS) or Jacobian is simplified for the passive scalar system
ADx = b – Ax*=-res ~ MDx
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 47: Deep Dive on EBVC: Example Case
For a mid-term set of example cases, we have selected a flow past a two-dimensional cylinder at a Reynolds number of 150
Mesh and input files can be found in the Nalu/examples/street directory
Familiarize yourself with this physics set via literature surveys
  As a starting place, see: https://en.wikipedia.org/wiki/Kármán_vortex_street
  Also look at the Canvas Nalu lecture notes for a brief write-up
In this test case, we have added a passive scalar field whose inflow is zero and wall boundary condition unity. For your final project, feel free to modify inflow and wall parameters as you choose.
Note that this case uses a conformal hybrid mesh, or a mesh of disparate element topologies, Quad4 and Tri3
See: https://canvas.stanford.edu/courses/137697/files/folder/additional_reading?preview=7730176

## Slide 48: Deep Dive on EBVC: Example Viz (Passive Scalar)
Hybrid mesh (quad4/tri3)

## Slide 49: Some Interesting Configurations: Flow Parameters
- inflow_boundary_condition: bc_left
target_name: Inflow
inflow_user_data:
velocity: [1.0,0.0]
mixture_fraction: 0.0
Controls the flow Reynolds number (along with density and viscosity)
- symmetry_boundary_condition: bc_top_bottom
target_name: Sides
symmetry_user_data:
“slip”, or zero tangential velocity at top and bottom; change to a wall for a duct entrance example
- wall_boundary_condition: bc_cylinder
target_name: Cylinder
wall_user_data:
velocity: [0.0,0.0]
mixture_fraction: 1.0
Fixed velocity; change to rotating via user function?
﻿Time_Integrators:
- StandardTimeIntegrator:
name: ti_1
start_time: 0
termination_step_count: 2000
time_step: 1.0e-3
time_stepping_type: adaptive
time_step_count: 0
second_order_accuracy: yes
second_order_accuracy: yes/no

## Slide 50: Some Interesting Configurations
- limiter:
velocity: yes
mixture_fraction: no
- laminar_schmidt:
mixture_fraction: 0.9
- peclet_function_form:
velocity: tanh
mixture_fraction: tanh
- peclet_function_tanh_transition:
velocity: 2.0
mixture_fraction: 1000.0
- peclet_function_tanh_width:
velocity: 4.0
mixture_fraction: 100.0
Upwind using projected nodal gradients is limited

## Slide 51: Deep Dive on EBVC
Recall, EBVC is a discretization scheme that:
  Iterates over locally-owned nodes for Time/Source/etc. (volumetric-based terms)
  Iterates over locally-owned edges for Advection/Diffusion/etc. (integrated by parts terms)
  Below is the patch of elements connected to node 2 (a global matrix row number)
  Area vector at the edge and dual volume at the node require the node:element connectivity whose quantities are determined in a pre-processing step
8
5
6
1
2
3
7
4
n1
n2
n3
e1
e2
e3
e4
n4
n5
Sample patch of elements
Note: No expectation of nodal ordering..

## Slide 52: Deep Dive on EBVC: Node and Edge-loops
Recall, EBVC is a discretization scheme that:
  Iterates over locally-owned nodes for Time/Source/etc. (volumetric-based terms)
  Iterates over locally-owned edges for Advection/Diffusion/etc. (integrated by parts terms)
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n2
n1 (L)
n2 (R)
e1

## Slide 53: Deep Dive on EBVC: Implicit Time Discretization
Let us define a general implicit time integrator that is A-stable
  For y’ = k y ; y(0) = 1; y(t) = ekt solution approaches zero as time increases for k < 0
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over a nodal iteration
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2
n2

## Slide 54: Deep Dive on EBVC: Implicit Time Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/ScalarMassBDF2NodeSuppAlg.C
Note the implicit term

## Slide 55: Deep Dive on EBVC: Source Term Discretization
Source terms for the edge-based scheme are also assembled over a nodal loop
Note that in this scheme, we are using single point quadrature, i.e., the function is evaluated at a single point
p = 2N -1
  Where N is the number of integration points and p is the polynomial order
  For a linear basis, using one-point quadrature is design-order
n2

## Slide 56: Deep Dive on EBVC: Source Term Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/user_functions/VariableDensityMixFracSrcNodeSuppAlg.C

## Slide 57: Deep Dive on EBVC: Advection Discretization (no stabilization)
For advection, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
Recall, that the mass flow rate at an integration point is prescribed
Moreover, since the integration point is at the edge mid-point, fip = (fR + fL)/2
This is a central- or Galerkin-based advection operator; shown in conservative form
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1
Note: Advection term must be in divergence form….

## Slide 58: Deep Dive on EBVC: Advection Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/AssembleScalarEdgeSolverAlgorithm.C
This routine includes advection and diffusion

## Slide 59: Upwind Operators
Upwind advection operators can provide diagonal dominance (at the cost of accuracy)
However, upwind operators, even if higher-order, are numerically diffuse
Higher-order upwind (second-order in space) can be obtained on an unstructured mesh by use of projected nodal gradients and extrapolation:
j-1
j
j+1
Zj+1/2
Zj-1/2
for u>0
a is a blending
parameter
“as the wind blows”

## Slide 60: Pseudo Higher-order Upwind
Blending extrapolated upwind with central (ZL+ZR)/2 provides:
Slope limiting required when gradients are not smooth (Berger et al, 2005, 43rd AIAA)
for u>0
j-2 | j-1 | j | j+1 | j+2 | a | 
1/4 | -5/4 | +3/4 | +1/4 | 0 | 1 | >0
0 | -1/4 | -3/4 | +5/4 | -1/4 | 1 | >0
+1/6 | -6/6 | +3/6 | +2/6 | 0 | 1/2 | <0
0 | -2/6 | -3/6 | +6/6 | -1/6 | 1/2 | <0
for u<0
Resulting
1-D Stencil

## Slide 61: Deep Dive on EBVC: Diffusion Discretization
For diffusion, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1

## Slide 62: Deep Dive on EBVC: Diffusion Discretization
The edge-based diffusion operator is a bit more complex in that we are computing a gradient at the integration point while using two nodes, the left and right
In many practical meshes, the distance vector between the edges (dxj) and the edge area vector will not be perfectly orthogonal
This non-orthogonality causes inaccuracy when using a simplified approach
The non-orthogonality approach of Jasek (Ph.D. Imperial College) is a standard cell-centered approach that has been adopted for edge-based schemes
  CC and EBVC are each two-state schemes and share non-orthogonality issues
n2 (L)
n3 (R)
e2

## Slide 63: Deep Dive on EBVC: Diffusion Discretization (code)
https://github.com/NaluCFD/Nalu/blob/master/src/AssembleScalarEdgeDiffSolverAlgorithm.C

## Slide 64: Types of Boundary Conditions
Inflow: values are known and enforced via a Dirichelp
Open: pressure known: flow in or out of the domain; zero gradient for diffusion
Wall: values are known and enforced via a Dirichlet
Symmetry: Normal stress specified; tangential stress zero
Non-conformal: hybrid DG/CVFEM
“overset”: Constraint-based
See: https://nalu.readthedocs.io/en/latest/source/theory/boundaryConditions.html

## Slide 65: Common low-Mach Discretization Approaches: Conclusions
Two-state methods, e.g., cell-centered and EBVC are attractive due to simplicity, however, suffer from non-orthogonality issues in the diffusion operator
Generally, CC or EBVC is 2x faster on a given mesh size
Less accurate/stable on generalized unstructured mesh topologies
Better diffusion operator on high-aspect ratio meshes

## Slide 66
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE
Stanford ME469: Common low-Mach Discretization Approaches: CVFEM/FEM

## Slide 67: Deep Dive on CVFEM
Recall, CVFEM is a discretization scheme that:
  Iterates over locally-owned elements for Time/Source/etc. (volumetric-based terms)
  Iterates over locally-owned elements for Advection/Diffusion/etc. (integrated by parts terms)
  Below is the patch of elements connected to node 2 (a global matrix row number)
8
5
6
1
2
3
7
4
Sample patch of elements
Note: Time and source terms can also be evaluated at nodes without loss of accuracy

## Slide 68: Deep Dive on CVFEM: Element-loops
For each element, recall that a dual volume has been constructed
Volume-based contributions are evaluated at the subcontrol volume integration points (diamonds)
Surface-based contributions are evaluated at the subcontrol surface integration points (triangles)
We define an isoparametric element than ranges from -1:1 in the x- (x-direction) and h- (y-direction) direction
Basis Functions for a Quad4
For example, the isoparametric coordinate for ip 1 is (0.0, -0.5)

## Slide 69: Deep Dive on CVFEM: Implicit Time Discretization
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over an element iteration and drives a consistent mass matrix with a full node:element:node connectivity
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2

## Slide 70: Deep Dive on CVFEM: Implicit Time Discretization
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over an element iteration and drives a consistent mass matrix with a full node:element:node connectivity
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2

## Slide 71: Deep Dive on CVFEM: Implicit Time Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarMassElemKernel.C

## Slide 72: Deep Dive on CVFEM: Source Term Discretization
Source terms for CVFEM are also assembled over an element or nodal loop
In some cases, the source term is complex, i.e., includes gradients, which drives either a nodal assembly of these quantities to the nodes or local evaluation

## Slide 73: Deep Dive on CVFEM: Source Term Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/user_functions/SteadyThermal3dContactSrcElemKernel.C

## Slide 74: Deep Dive on CVFEM: Advection Discretization (no stabilization)
For advection, we have transformed the volume integral to a surface integration
Therefore, a patch of elements are required for the full assembly at node 2
Recall, that the mass flow rate at an integration point is prescribed
Integration points can also be shifted from the subcontrol surface to the edge mid-poiny (while still using the integration point area vector)
This is a central- or Galerkin-based advection operator
Note:
Common to integrate-by-parts, however, not required
Advection term need not be in divergence form (non-conserved form is suitable)

## Slide 75: Deep Dive on CVFEM: Advection Discretization Non-Conserved Form
The advection term can be integrated by parts, or not; moreover, the PDE can drive a non-conservative equation form
IBP – or not…
This is now a choice
Non-conserved form, unlike cell-centered FV, poses no complexity

## Slide 76: Deep Dive on CVFEM: Advection Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarAdvDiffElemKernel.C
This routine includes advection and diffusion
Recall that integration point value is provided by nodal loop over the underlying nodal basis for this element
Also note that this routine is valid for all types of supported elements – both low- and higher-order
Basis Functions for a Quad4

## Slide 77: Deep Dive on CVFEM: Diffusion Discretization
For diffusion, we have transformed the volume integral to a surface integration
Therefore, a patch of elements are required for the full assembly at node 2
Note that the CVFEM approach is absent any non-orthogonality corrections;
However, high aspect ratio elements are now challenging…

## Slide 78: Deep Dive on CVFEM: Diffusion Discretization (code)
https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarAdvDiffElemKernel.C

## Slide 79: Deep Dive on Nodal Gradient Operator: An Alternative View
Recall, that the edge-based diffusion operator, and for some choices for the advection operator, a nodal gradient is required
What is a nodal gradient? As formerly described in the Computing Gradients lecture, in a cell-centered context we obtained this via a number of ways, e.g., Green-Gauss, Least Squares, etc.
Let’s take another view…
First, the gradient of a function (other than linear) is discontinuous, i.e., the value at a shared element face depends on which element is used to compute the gradient
Therefore, we can view the nodal gradient a continuous at the nodes and discontinuous within the elements
Let’s minimize this difference:
by solving:
Lumped-mass

## Slide 80: Deep Dive on FEM
Recall, FEM is a discretization scheme that:
  Iterates over locally-owned elements for Time/Source/etc (volumetric-based terms)
  Iterates over locally-owned elements for Advection/Diffusion/etc. (integrated by parts terms)
  Below is the patch of elements connected to node 2 (a global matrix row number)
8
5
6
1
2
3
7
4
Sample patch of elements
Note: Single integration point location for all terms

## Slide 81: Deep Dive on FEM: Element-loops
For each element, we have a set of integration or quadrature points (no dual-notion)
We define an isoparametric element than ranges from -1:1 in the x- (x-direction) and h- (y-direction) direction
Gaussian quadrature on a -1:1 range is defined, +/- sqrt(3)/3
Basis Functions for a Quad4
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 82: Deep Dive on FEM: Implicit Time Discretization
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over an element iteration and drives a consistent mass matrix with a full node:element:node connectivity
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 83: Deep Dive on FEM: Source Term Discretization
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2
Source terms for FEM are assembled over an element loop
In some cases, the source term is complex, i.e., includes gradients, which drives either a nodal assembly of these quantities to the nodes or local evaluation

## Slide 84: Deep Dive on FEM: Advection Discretization
Advection terms for FEM are assembled over an element loop
The advection term can be integrated by parts, or not; moreover, the PDE can drive a non-conservative equation form
IBP – or not…
This is now a choice
Non-conserved form, like CVFEM, poses no complexity
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 85: Deep Dive on FEM: Diffusion Discretization
For diffusion, we will again use the nodal basis to support a diffusion operator
Integration-by-parts is desired to remove the second-derivative requirement that would not be possibly for a linear basis
Note that the FEM approach is absent any non-orthogonality corrections
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 86: Element Integration: Physical to Transformed Space
Let us define a linear basis over a representative two-dimensional quadrilateral with iso-parametric range of x: -1:+1 and h: -1:+1
Goal: Evaluate an integral:
Change of variables:
Transformation:
|J| is determinant of the transformation matrix
With weight wg

## Slide 87: Deep Dive on FEM: Discretization Kernels (Code)
Time
  https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarMassFemKernel.C
Advection
  https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarAdvFemKernel.C
Diffusion
  https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarDiffFemKernel.C

## Slide 88: Common low-Mach Discretization Approaches: Conclusions
FEM provides a machinery to provide accurate discretizations on non-ideal meshes, however, the same diffusion operator suffers on high-aspect ratio meshes
CVFEM is a hybrid method that contains the likeable attributes of both FV and FEM (same high-aspect ratio diffusion operator finding)

## Slide 89
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE
Stanford ME469: Common low-Mach Discretization Approaches: Comparisons

## Slide 90: Philosophy: Bridges, not Walls
Me469 Tenant: Let’s work to understand how each method relate to one another
FVM
GFEM
CVFEM
FD

## Slide 91: Laminar Backstep
X-component of velocity
Vertical line represents one-D
line plot location
Laminar back step (Re = 389 based on step height) comparing two code implementations for CVFEM (Sierra/Fuego and Sierra Aria), FEM (within Aria – here termed, “hybrid” FEM, or HFEM – essentially, the same low-Mach CVFEM approach with full integration-by-parts).

## Slide 92: Laminar Jet
Y-component of velocity

## Slide 93: Order-of-Accuracy
Difficult two dimensional variable density low-Mach flow using method of manufactured solutions; DOFS: u, v, p and Z; density = f(Z)
CVFEM
FEM

## Slide 94: Isothermal Taylor-Vortex Decay
Domino, 2014 “A comparison between low-order and higher-order low-Mach discretization approaches”, Proceedings of CTR Summer Program.
Exercising the low-and high-order (P=1 and P=2 CVFEM) along with EBVC with and without pseudo-higher-order upwind)

## Slide 95: Non-Conformal Laplace Verification

## Slide 96: Hybrid Meshes, Even for LES!
Hybrid mesh study based on Ham and Iaccarino, CTR Annual Brief, 2006, found that simulations were extremely sensitive to mesh topology
  Non-symmetric time mean flow found for cell-centered; better for the CTR node-centered formulation
Native CVFEM and EBVC are both symmetric in mean quantities
B
T
Domino, et. al, “The suitability of hybrid meshes for low-Mach large-eddy simulation” Stanford CTR Summer Program, 2018

## Slide 97: 5m JP-8 Pool Fire Validation
Novel participating media radiation solver verification (Tet4, Hex8, Hex27): EBVC and CVFEM, however, based on Streamwise Upwind Petrov Galerkin (SUPG), Burns, 1997
1.7m
Domino et al. “Predicting large-scale pool fire dynamics using an unsteady flamelet- and large-eddy simulation-based model suite", Physics of Fluids, 2021 (Editor's pick: August 4, 2021).
+
Notes: The former V&V method required experts choosing the appropriate LES models (Smagorinsky, Ksgs, and WALE). In most cases, no one (sadly) really evaluates this model-form error.
Choosing multiple models in a V&V credibility effort required coding of the said models, verification of the models, and maintenance, i.e., $$$$. Is there a better way to manage structural uncertainty for LES? Yes, my V&V project in partnership with Stanford is doing this..
Background: In LES, we desire to close the subgrid stress (SGS), or Tau_ij.
This SGS stress is a symmetric tensor that is positive-definite. As such, we can perform an eigenvalue decomposition. The eigenvectors provide an orthonormal basis while the eigenvalues represent the ”weight” towards the limiting types of turbulence: one-component (rods), two-component (pancakes) and three-component (isotropic and circular).
The triangle is a “barycentric triangle” that represents a linear mapping between the eigenvalues to a picture. The shaded triangle is a real simulation where we are probing a point in space and plotting the eigenvalue decomposition (open jet). Any viable model ever dreamed of must fit inside this triangle.
By perturbing the eignevalues and eigenvectors, we can evaluate uncertainty in the LES model. This is really powerful.