## Slide 1
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE
Stanford ME469: Common low-Mach Discretization Approaches

## Slide 2: Common low-Mach Discretization Approaches: Outline
The Concept of Meshing
Why Unstructured?
Unstructured Element Typoes
Model PDE for Discretization
Finite Element Method (FEM)
Control-Volume Finite Element Method (CVFEM)
Edge-based Vertex-Centered (EBVC)
Cell-centered Finite Volume (FV)
Staggered arrangement
Conclusions

## Slide 3: Mesh-based Methods Basic Concept: Sub-divide domain into Finite Elements
Define basis within the domain:
Ge
We
We
Quad4Patch
Tri3Patch
Note: Exterior of domain is faceted
Note: Interface between Tri3/Quad4 block is non-conformal

## Slide 4: Structured vs Unstructured
Many times, the canonical flows of interest are in simplified geometries that allow for cartesian meshes – with “stair-stepping”
Ret 395 plane-channel (Jofre, Domino, Iaccarino, 2018)
https://www.itascainternational.com/software/introduction-to-meshing
Often times, not!
RANS-based backward facing step (Domino, 2012)

## Slide 5: Reality: Meshing time for complex applications remains a significant bottleneck!
Many applications of interest to SNL contain complex geometries
low-Mach fluids users interested in high-quality simulation results tend towards hexahedral-based topologies (if possible)
However, if a scheme is “design-order” accurate, any topology may suffice as it is simply a matter of mesh size and efficiency – not unlike the active discussion on low- vs higher-order
Sometimes, the penetration of a low-Mach fluids physics addition in common analysis is high as the meshing can be prohibitively complex
UUR Example: Vestas V27 225 kw hybrid low-order hex/tet/pyr/wedge
Very complex world – stair-stepped!

## Slide 6: Examples of Various Topologies
Hex8
Tet4
Pyramid5
Wedge6
Arbitrary
Higher-order promoted elements (Hex27, Tet10, Wedge16, Hex64, etc.)

## Slide 7: In Fairness…. The Carbon-Capture Multidisciplinary Simulation Center
http://ccmsc.utah.edu/about.html
15MW coal-fired boiler volume rendered image of large (90 mm) particles
Staggered schemes have been demonstrated to support complex applications
Cut-cells and embedded approaches help

## Slide 8: Fundamentals of Discretization (Review)
Given a partial differential equation (PDE) and associated volumetric form:
Applying Gauss Divergence provides the standard finite volume form:
We can also multiple PDE by an arbitrary test function, w, and integrate over a volume,
Next, integrate by parts and apply
Gauss-Divergence:
Sometimes, you see T as Th - the trial space

## Slide 9: The Finite Element Method (FEM)
Consider an alternative approach in which a finite element method (FEM) is employed
Define an underlying nodal basis with the element:
Gaussian Quadrature is used
On a -1:1 range, +/- sqrt(3)/3
Consider a simple heat conduction model PDE,
Integrate using a test function,
Integration-by-parts (with G-D) provides:
Iterate element quadrature points
Note that N can be arbitrary in order (shown here for a linear)

## Slide 10: The Hybrid Control-Volume Finite Element Method (CVFEM)
A combination between the edge-based vertex-centered and FEM is the method known as Control Volume Finite Element ()
A dual mesh is constructed to obtain flux and volume quadrature locations
As with FEM, a basis is defined:
Dual-volume definition
Integration-by-parts over test function w:
However, define a test function, w, as a piece-wise constant function (Heavyside) to be 1 inside the dual volume and 0 outside. Gradient is a Dirac-delta function:
Leading to:

## Slide 11: Control-Volume Finite Element Method Attributes
The CVFEM method, therefore, is a finite volume scheme that is locally conservative, i.e., momentum leaving one dual volume face enters the adjacent dual volume
However, the gradient operator, like its FEM counterpart is absent of any error due to non-orthogonality
Since the test-function, w, is different from the underlying basis representation, this method can be considered a Petrov-Galerkin method
The method can also be promoted in polynomial space
Spectral convergence
Dual-volume for promoted quad4
P=1 (left) and P=4 (right)
Helium plume (VR-density)

## Slide 12: Dual Volume Definitions for Hybrid Meshes
Domino, et. al, “An assessment of atypical mesh topologies for low-Mach large-eddy simulation” 2019

## Slide 13: Recent Generalized Unstructured Findings
Domino, et. al, “An assessment of atypical mesh topologies for low-Mach large-eddy simulation” 2019

## Slide 14: Equal Order Interpolation Edge-Based Vertex-Centered (EBVC) Finite Volume
Same grad-op as CC:
Iterate nodes for volume contributions
Iterate edges for surface flux contribution
All primitives are collocated at the vertices of the elements with equal-order interpolation
A dual mesh is constructed to obtain flux and volume quadrature locations
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
Surface quadrature point (area summed to edge)
Volume quadrature point (sub-vol summed to node)
nj
Dual-volume definition
Edge-based stencil
TL
TR

## Slide 15: Equal-Order Interpolation Cell-Centered (CC) Finite Volume
Consider a simple heat conduction model PDE,
Integrate over a control volume and use Gauss-Divergence,
Iterate element cell-centers for volume contributions (time/source)
Iterate element faces for surface flux contribution
All primitives are collocated at the cell-center of the element with equal-order interpolation
Classic two-state, “L” and “R” approach provides spatially second-order accuracy
TL
TR
Surface
quadrature point
with:
nj

## Slide 16: Typical Failings for Two-State Discretization Methods
With two points, only a linear basis can be used.
Therefore, unstructured CC and EBVC are limited to second-order spatial accuracy
Non-orthogonality is problematic for gradient-operator
Above, GjT is a projected nodal gradient at the cell-center, or vertex center:
Non-orthogonality is simply defined as the mis-alignment of the distance vector between the two ”L” and “R” states and the surface normal
Both edge- and cell centered-based schemes show degraded accuracy on typical production meshes
Several non-orthogonality approaches are available, for the best source, see Jasak
  Jasak, “Error analysis and error estimation for the finite volume method with applications to fluid flow”, Imperial College Dissertation, 1996
nj
Dxj
With area vector defined by:

## Slide 17: Classic Staggered Finite Volume
Velocity degree-of-freedom is staggered relative to pressure and other primitives, e.g., enthalpy, mixture fraction, etc.
Stencil for CC-quantities
Stencil for x-velocity
Stencil for y-velocity
PN
PS

## Slide 18: Attributes of a Staggered Scheme
By design, non-orthogonality is absent, however, complex geometry will be stair-stepped
From a fluids perspective, the operators are ideal, i.e., pressure gradient for momentum is compact, e.g., (PE – PW)Dx-1
  As will be seen in future lecture topics, the skew-adjoint nature of the Divergence operator, D, and Gradient operator, G, allows for a Laplace operator, L = DG
Can be extended to higher-order
Frequently, meshing complex geometries can be extremely difficult (consider our V27 example)

## Slide 19: Model Passive Scalar Transport
Time/Src/Advection/Diffusion equation for scalar f
Here, w is the weight function, or an arbitrary function that is differentiable (at least once)
In this example, let density, velocity, and diffusive flux coefficient be prescribed
This equation, with a prescribed velocity, can be used to model trace species contaminant transport, smoke, etc.
The above equation is termed a weighted-residual statement of the original PDE

## Slide 20: Model Passive Scalar Transport; Heaviside Test Function
Time/Src/Advection/Diffusion equation for scalar f
The CVFEM and EBVC test function meets our requirement in that it is differentiable once
This definition also allows us to view such methods as Petrov Galerkin schemes

## Slide 21: Deep Dive on EBVC
Recall, EBVC is a discretization scheme that:
  Iterates over nodes for Time/Source/etc. (volumetric-based terms)
  Iterates over edges for Advection/Diffusion/etc. (integrated by parts terms)
  Below is the patch of elements connected to node 2 (a global matrix row number)
  Area vector at the edge and dual volume at the node require the node:element connectivity whose quantities are determined in a pre-processing step
8
5
6
1
2
3
7
4
n1
n2
n3
e1
e2
e3
e4
n4
n5
Sample patch of elements
Note: No expectation of nodal ordering..

## Slide 22: Deep Dive on EBVC: Node and Edge-loops
Recall, EBVC is a discretization scheme that:
  Iterates over nodes for Time/Source/etc. (volumetric-based terms)
  Iterates over edges for Advection/Diffusion/etc. (integrated by parts terms)
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n2
n1 (L)
n2 (R)
e1

## Slide 23: Deep Dive on EBVC: Implicit Time Discretization
Let us define a general implicit time integrator that is A-stable
  For y’ = k y ; y(0) = 1; y(t) = ekt solution approaches zero as time increases for k < 0
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over a nodal iteration
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2
n2

## Slide 24: Deep Dive on EBVC: Implicit Time Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/ScalarMassBDF2NodeSuppAlg.C
Note the implicit term

## Slide 25: Deep Dive on EBVC: Source Term Discretization
Source terms for the edge-based scheme are also assembled over a nodal loop
Note that in this scheme, we are using single point quadrature, i.e., the function is evaluated at a single point
p = 2N -1
  Where N is the number of integration points and p is the polynomial order
  For a linear basis, using one-point quadrature is design-order
n2

## Slide 26: Deep Dive on EBVC: Source Term Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/user_functions/VariableDensityMixFracSrcNodeSuppAlg.C

## Slide 27: Deep Dive on EBVC: Advection Discretization (no stabilization)
For advection, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
Recall, that the mass flow rate at an integration point is prescribed
Moreover, since the integration point is at the edge mid-point, fip = (fR + fL)/2
This is a central- or Galerkin-based advection operator
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1
Note: Advection term must be in divergence form….

## Slide 28: Deep Dive on EBVC: Advection Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/AssembleScalarEdgeSolverAlgorithm.C
This routine includes advection and diffusion

## Slide 29: Deep Dive on EBVC: Diffusion Discretization
For diffusion, we have transformed the volume integral to a surface integration
Therefore, a patch of edges are required for the full assembly at node 2
n1
n2
n3
e1
e2
e3
e4
n4
n5
n2 (L)
n3 (R)
e2
n1 (L)
n2 (R)
e1

## Slide 30: Deep Dive on EBVC: Diffusion Discretization
The edge-based diffusion operator is a bit more complex in that we are computing a gradient at the integration point while using two nodes, the left and right
In many practical meshes, the distance vector between the edges (dxj) and the edge area vector will not be perfectly orthogonal
This non-orthogonality causes inaccuracy when using a simplified approach
The non-orthogonality approach of Jasek (Ph.D. Imperial College) is a standard cell-centered approach that has been adopted for edge-based schemes
  CC and EBVC are each two-state schemes and share non-orthogonality issues
n2 (L)
n3 (R)
e2

## Slide 31: Deep Dive on EBVC: Diffusion Discretization (code)
https://github.com/NaluCFD/Nalu/blob/master/src/AssembleScalarEdgeDiffSolverAlgorithm.C

## Slide 32: Deep Dive on EBVC: Example Case
For a mid-term set of example cases, we have selected a flow past a two-dimensional cylinder at a Reynolds number of 150
Mesh and input files can be found in the Nalu/examples/street directory
Familiarize yourself with this physics set via literature surveys
  As a starting place, see: https://en.wikipedia.org/wiki/Kármán_vortex_street
In this test case, we have added a passive scalar field whose inflow is zero and wall boundary condition unity. For your final project, feel free to modify inflow and wall parameters as you choose.
Note that this case uses a conformal hybrid mesh, or a mesh of disparate element topologies, Quad4 and Tri3

## Slide 33: Deep Dive on CVFEM
Recall, CVFEM is a discretization scheme that:
  Iterates over elements for Time/Source/etc. (volumetric-based terms)
  Iterates over elements for Advection/Diffusion/etc. (integrated by parts terms)
  Below is the patch of elements connected to node 2 (a global matrix row number)
8
5
6
1
2
3
7
4
Sample patch of elements
Note: Time and source terms can also be evaluated at nodes without loss of accuracy

## Slide 34: Deep Dive on CVFEM: Element-loops
For each element, recall that a dual volume is constructured
Volume-based contributions are evaluated at the subcontrol volume integration points (diamonds)
Surface-based contributions are evaluated at the subcontrol surface integration points (triangles)
We define an isoparametric element than ranges from -1:1 in the x- (x-direction) and h- (y-direction) direction
Basis Functions for a Quad4
For example, the isoparametric coordinate for ip 1 is (0.0, -0.5)

## Slide 35: Deep Dive on CVFEM: Implicit Time Discretization
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over an element iteration and drives a consistent mass matrix with a full node:element:node connectivity
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2

## Slide 36: Deep Dive on CVFEM: Implicit Time Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarMassElemKernel.C

## Slide 37: Deep Dive on CVFEM: Source Term Discretization
Source terms for CVFEM are also assembled over an element or nodal loop
In some cases, the source term is complex, i.e., includes gradients, which drives either a nodal assembly of these quantities to the nodes or local evaluation

## Slide 38: Deep Dive on CVFEM: Source Term Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/user_functions/SteadyThermal3dContactSrcElemKernel.C

## Slide 39: Deep Dive on CVFEM: Advection Discretization (no stabilization)
For advection, we have transformed the volume integral to a surface integration
Therefore, a patch of elements are required for the full assembly at node 2
Recall, that the mass flow rate at an integration point is prescribed
Integration points can also be shifted from the subcontrol surface to the edge mid-poiny (while still using the integration point area vector)
This is a central- or Galerkin-based advection operator
Note: Advection term need not be in divergence form….

## Slide 40: Deep Dive on CVFEM: Advection Discretization (Code)
https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarAdvDiffElemKernel.C
This routine includes advection and diffusion

## Slide 41: Deep Dive on CVFEM: Diffusion Discretization
For diffusion, we have transformed the volume integral to a surface integration
Therefore, a patch of elements are required for the full assembly at node 2
Note that the CVFEM approach is absent any non-orthogonality corrections

## Slide 42: Deep Dive on CVFEM: Diffusion Discretization (code)
https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarAdvDiffElemKernel.C

## Slide 43: Deep Dive on FEM
Recall, FEM is a discretization scheme that:
  Iterates over elements for Time/Source/etc (volumetric-based terms)
  Iterates over elements for Advection/Diffusion/etc. (integrated by parts terms)
  Below is the patch of elements connected to node 2 (a global matrix row number)
8
5
6
1
2
3
7
4
Sample patch of elements
Note: Single integration point location for all terms

## Slide 44: Deep Dive on FEM: Element-loops
For each element, we have a set of integration or quadrature points (no dual-notion)
We define an isoparametric element than ranges from -1:1 in the x- (x-direction) and h- (y-direction) direction
Gaussian quadrature on a -1:1 range is defined, +/- sqrt(3)/3
Basis Functions for a Quad4
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 45: Deep Dive on FEM: Implicit Time Discretization
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over an element iteration and drives a consistent mass matrix with a full node:element:node connectivity
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 46: Deep Dive on FEM: Implicit Time Discretization
Backward Euler (two state) and is first-order accurate (A-stable)
BDF2 (three state) is second-order accurate (A-stable)
This term is assembled over an element iteration and drives a consistent mass matrix with a full node:element:node connectivity
For uniform time steps:
g1 = 3/2
g2 = -2
g3 = 1/2
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 47: Deep Dive on FEM: Source Term Discretization
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2
Source terms for FEM are assembled over an element loop
In some cases, the source term is complex, i.e., includes gradients, which drives either a nodal assembly of these quantities to the nodes or local evaluation

## Slide 48: Deep Dive on FEM: Advection Discretization
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2
Advection terms for FEM are assembled over an element loop
The advection term can be integrated by parts, or not; moreover, the PDE can drive a non-conservative equation form
IBP
Non-conserved form, like CVFEM, poses no complexity

## Slide 49: Deep Dive on FEM: Diffusion Discretization
For diffusion, we will again use the nodal basis to support a diffusion operator
Integration-by-parts is desired to remove the second-derivative requirement that would not be possibly for a linear basis
Note that the FEM approach is absent any non-orthogonality corrections
5 [4] (-1,1)
6 [3] (1,1)
2 [1] (-1,-1)
3 [2] (1,-1)
1
2
4
3
1
2

## Slide 50: Deep Dive on FEM: Numerical Integration
Transform the integral via a change of variables from physical space to isoparametric space
And apply Gaussian Quadrature over a -1:1 mapping (for a Quad/Hex-based element) by introducing quadrature weights

## Slide 51: Deep Dive on FEM: Discretization Kernels (Code)
Time
  https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarMassFemKernel.C
Advection
  https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarAdvFemKernel.C
Diffusion
  https://github.com/NaluCFD/Nalu/blob/master/src/kernel/ScalarDiffFemKernel.C

## Slide 52: Common low-Mach Discretization Approaches: Conclusions
Two-state methods, e.g., cell-centered and EBVC are attractive due to simplicity, however, suffer from non-orthogonality issues in the diffusion operator
FEM provides a machinery to provide accurate discretizations on non-ideal meshes, however, the same diffusion operator suffers on high-aspect ratio meshes
CVFEM is a hybrid method that contains the likeable attributes of both FV and FEM (same high-aspect ratio diffusion operator finding)
Staggered arrangement is well suited for a class of fluid mechanics applications where low-order or simple geometries are found