## Slide 1: Stanford ME469: Nalu Suggested Homework #1 Discussion
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE

## Slide 2: Homework #1 Discussion: Outline
Discuss task 1: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Discuss task 2: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Discuss task 3: specified pressure pipe flow
Wait… a significant departure from task 3
Simple time/convection MMS for P=1
Simple time/convection MMS for P=2
Back to the pipe!
Conclusions

## Slide 3: Answer for Homework #1, Task 1 of 3
Task 1: Run Nalu/reg_tests/test_files/dgNonConformalThreeBlade
  Modify the input file to increase termination_step_count to ~500:
  Visualize the flow field with displacements activated and provide a single image at the final step count.
  How does modification of the blade rotation (omega) affect the time step?
    time_stepping_type: adaptive
    Courant# = URTMDt/Dx with URTM=U-Vmesh
    As Vmesh increases, Dt decreases to meet a fixed Courant number specification of 2
  Report any modifications that resulted in catastrophic behavior, i.e., the simulation diverged. Document how you caused the simulation to diverge.
    Too large of a time step given rotation, omega
    Initial time step too large
    No open bc specified (rendering flow a low-speed compressible configuration)
Time_Integrators:
- StandardTimeIntegrator:
name: ti_1
start_time: 0
termination_step_count: 500
time_stepping_type: adaptive
time_step_control:
target_courant: 2.0
time_step_change_factor: 1.15

## Slide 4: Answer for Homework #1, Task 2 of 3
Task 2: Run Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
  Modify the input file to increase termination_step_count to ~500.
  Visualize the temperature, velocity, and radiative file (your choice) and provide a single image at the final step count.
  Modify the gravity constant such that the Rayleigh number 10x, 100x, etc. Report any findings; does the code benefit from a modification of initial time step size?
    Increased velocity magnitude from 0.16, 0.46, 1.5, and 3.7 m/s for gx1, gx10, gx100, gx1000
  What happens if you change the velocity hybrid parameter to: velocity: 0.0
    Far less advection stabilization is added. Former value of unity allows for velocity oscillations for cell Peclet number > 2
    see: https://nalu.readthedocs.io/en/latest/source/theory/advectionStabilization.html
options:
- hybrid_factor:
velocity: 0.0
enthalpy: 1.0
Time_Integrators:
- StandardTimeIntegrator:
name: ti_1
start_time: 0
termination_step_count: 500
time_stepping_type: adaptive
Ra = 106
Ra = 107
Ra = 108
Ra = 109
- user_constants:
gravity: [0.0, -9810.0, 0.0]
Ra ~ 109 velocity vector colored by temperature

## Slide 5: Answer for Homework #1 Task 3: Specified Pressure Drop Laminar Pipe Flow:
First, let’s think about this quadratic solution a bit more….

## Slide 6: Simple One-D MMS Example; General Form
Consider a simple diffusion equation:
with a presumed, or manufactured solution:
Gauss-Divergence
Discrete flux-based form:
With error:

## Slide 7: Simple One-D MMS Example; Nodal Assemble of Source Term
We will use a linear basis and solve this system over a small patch of linear bar elements
x
x
x
node = 0
1
2
3
Boundary Conditions:
f(x=0) = 0
f(x=3) = 9
Dx = 1
Recall general Eq:
Simplified 1-D equation (Vscv = A*Dx/2)
First, assign lhs and rhs to zero, iterate subcontrol volume ips to assemble right-hand side source term:
Node 0
Node 1
Node 2
Node 3

## Slide 8: Simple One-D MMS Example; Edge-based Assemble of Diffusion
x
x
x
node = 0
1
2
3
Dx = 1
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
x
0
1
Edge 1
We will use a linear basis and solve this system over a small patch of linear bar elements

## Slide 9: Simple One-D MMS Example; Edge-based Assemble of Diffusion
x
x
x
node = 0
1
2
3
Dx = 1
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
x
1
2
Edge 2
We will use a linear basis and solve this system over a small patch of linear bar elements

## Slide 10: Simple One-D MMS Example; Edge-based Assemble of Diffusion
x
x
x
node = 0
1
2
3
Dx = 1
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
x
2
3
Edge 3
We will use a linear basis and solve this system over a small patch of linear bar elements

## Slide 11: Simple One-D MMS Example; Collect all of the lhs entries
Correct for BCs:
Correct for BCs
Fully assembled
system
Fully assembled
matrix
Solution is exact….. Linear basis exactly captures a quadratic solution

## Slide 12: Simple One-D MMS Example; General Form (New MMS)
Consider a simple diffusion equation:
with a presumed, or manufactured solution:
Gauss-Divergence
Discrete flux-based form:
With error:
x3
3x2

## Slide 13: Simple One-D MMS Example; General Form (New MMS)
Consider a simple diffusion equation:
with a presumed, or manufactured solution:
Gauss-Divergence
Discrete flux-based form:
With error:
x3
3x2
x4
4x3

## Slide 14: Simple One-D MMS Example; Quadratic CVFEM Assembly
We can use a quadratic basis and solve this system over a small patch of quadratic bar elements
node = 0
2
4
New promoted nodes “live” at the Gauss-Lobatto points while dual volume lives at the Gauss-Lagendre points: +/- sqrt(3)/3
Number of quadrature points for accurate integration scales as:
  2*numPts – 1 = polynomial order
  “2x2” quadrature will sufficiently integrate a quadratic basis
  Using single point quadrature would provide results that simply replicate uniform refinement of the low-order mesh.
Replicating the previous example with the new basis would again demonstrate exact prediction of nodal results!
3
1
O(P) basis: O(Dx)P+1 accuracy

## Slide 15: Example of a Quadratic Basis Function

## Slide 16: Answer for Homework #1 Task 3: Specified Pressure Drop Laminar Pipe Flow:
Location: https://github.com/spdomin/Present/tree/master/stanfordMe469/hw/one
You will modify the input file to provide the density, viscosity and pressure drop to achieve Ret = 10 and report on the differences between the simulation and analytical centerline velocity.
Specifications:
  Ret = 10
  Pipe diameter, D = 0.01 m
  Pipe Length, L = 0.1 m
Perform a global momentum balance to determine the pressure gradient. dp/dz as a function of the wall shear stress , tw.
  Momentum Balance: dp/dz = 4 tw / D
Given Ret = r ut D / m and tw = r (ut)2, where ut is the wall friction velocity, report the required pressure gradient required for the desired Ret = 10.
  Dp/Dz = 40.0e-3 Pa/m with DZ = 0.1 m
Modify the input file to specify the proper density, viscosity and open pressure specification (look for the pressure specification under open_user_data).
  r= 1.0 kg/m3 m= 1.0e-5
Run both the Hex8 and Tet4 input file and compare the simulation centerline velocity to the analytical result (feel free to derive or simply report the functional form).
  Analytical centerline is 2.5e-2 m/s
  Close, however, not exact for this second-order functional form due to geometry errors.
  Anyone try a 1x1x10 developing square pipe?
Capture any findings between the Hex8 and Tet4 simulation, e.g., simulation time, velocity component qualitative differences, convergence, etc.
- open_boundary_condition: bc_left
target_name: surface_2
open_user_data:
pressure: 40.0e-4
velocity: [0.0,0.0,0.0]
- open_boundary_condition: bc_right
target_name: surface_1
open_user_data:
pressure: 0.0
velocity: [0.0,0.0,0.0]
u(R) = uMax [1-(r/R)2]
uMax = Dp/Dz R2 / (4 m)
Hex wall-normal velocity is O(1e-15) while Tet is O(1e-6) m/s

## Slide 17: Pipe Flow Derivation

## Slide 18: Convince Yourself! Removal of Geometric Error Induced by the Pipe
Domino et al., “Verification for Multi-Mechanics Applications ”, AIAA, 2007
BCs:
Note: A common norm methodology to alleviate this slight confusion is to integrate over the domain using a consistent mass matrix:
For P=1, this procedure interpolates the quadratic solution using the underlying basis and reverts to displaying a clear second-order error for e vs Dx

## Slide 19: Homework #1 Discussion: Conclusions
A P-order underlying polynomial basis will provide a P+1 integrated error
Geometric fidelity for complex geometries is required for accurate solutions

## Slide 20: Homework #1 Discussion: A note on Art…
Georgia O’Keeffe, an American Artist: 1887-1986
https://www.kunm.org/post/landmark-okeeffe-painting-be-restored
Georgia O'Keeffe. Spring, 1948. Oil on canvas, 48 1/4 x 84 1/4 inches. Georgia O'Keeffe Museum. Gift of The Burnett Foundation. © Georgia O’Keeffe Museum. [1997.06.028]

## Slide 21: Homework #1 Discussion: A note on Art…
Who can create the best CFD art?

## Slide 22: Element Integration: Physical Space
Let us define a linear basis over a representative one-dimensional bar element with iso-parametric range of x: -1:+1
N1
N2
-1
+1
x
0

## Slide 23: Simple One-D MMS Example; General Form
Consider a simple time/convection equation:
with:
One-D; let r and ux be constant and unity:
Gauss-Divergence
Discrete flux-based form:
With error:

## Slide 24: Simple One-D MMS Example; Nodal Assemble of Source Term
We will use a linear basis and solve this system over a small patch of linear bar elements
x
x
x
node = 0
1
2
3
Boundary Conditions:
f(x=0) = 0
f(x=3) = 9
Dx = 1
Recall general Eq:
Simplified 1-D equation (unity density, x-velocity, and mesh spacing)
First, assign lhs and rhs to zero, iterate nodes to assemble right-hand side source term (2x):
Node 0
Node 1
Node 2
Node 3

## Slide 25: Simple One-D MMS Example; Edge-based assemble of convection
x
x
x
node = 0
1
2
3
Dx = 1
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
x
0
1
Edge 1
We will use a linear basis and solve this system over a small patch of linear bar elements

## Slide 26: Simple One-D MMS Example; Edge-based assemble of convection
x
x
x
node = 0
1
2
3
Dx = 1
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
x
1
2
Edge 2
We will use a linear basis and solve this system over a small patch of linear bar elements

## Slide 27: Simple One-D MMS Example; Linear CVFEM Assembly
x
x
x
node = 0
1
2
3
Dx = 1
Recall, simplified equation with RHS from source term already provided
Iterate elements with a simple left-hand side rule: += L and -=R
(note implicit conservation statement)
x
2
3
Edge 3
We will use a linear basis and solve this system over a small patch of linear bar elements

## Slide 28: Simple One-D MMS Example; Collect all of the lhs entries
Correct for BCs:
Solution is exact!

## Slide 29: Simple One-D MMS Example; General Form (new source)
Consider a simple time/convection equation:
with:
One-D; let r and ux be constant and unity:
Gauss-Divergence
Discrete flux-based form:
With error: