## Slide 1: Stanford ME469: Multiphysics Coupling
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE

## Slide 2: Multiphysics Coupling: Outline
Examples of multiphysics coupling with emphasis on fluids, PMR, and CHT
Monolithic vs Operator Split
Details of PMR/Fluids Coupling
Details of PMR/Thermal Coupling
Details of Fluids/Thermal Coupling
Verification
Stability
Conclusions

## Slide 3: We Live in a Multiphysics World
Intel® Xeon® Processor Scalable Family Thermal Mechanical Specifications and Design Guide
Fluid/Structure coupling:
  Wind turbines
  Wing fluttering, etc.
Non-isothermal fluids/participating media radiation:
  Fires,
  Natural gas and coal combustion,
  Smelting, ethylene production, etc.
Conjugate heat transfer:
  Object-in-fire
  Gas turbine fine cooling
Often times, we note a time and length scale disparity
  For example, consider heating a pan on a home burner
The coupling architect must generally choose between monolithic and split
For monolithic, the equations are provided, therefore, the challenge becomes managing a monolithic system solve, storage and code design
For operator split, there can be an “art” in determination of stable couplings due to Eignevalue spread
Wing Flutter on a 747
Erwin Platvoet Charles Baukal, P.E. John Zink Hamworthy Combustion

## Slide 4: Conjugate Heat Transfer Coupling
Convection Coef/Temp .
Common in engineering applications that require efficient heating or cooling of objects
Temperature
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
1 DOF/node
+ chemistry
Turbulent
Fluid Mechanics,
Combustion
15 dof/node
Thermal
Fluids
Tb
Turbulent pipe CHT
Tb

## Slide 5: Conjugate Heat Transfer Coupling, Equations
Favre-averaged static enthalpy equation:
Thermal heat conduction
Interface condition

## Slide 6: Fluid/CHT Coupling Verification
Unstructured heterogeneous mesh capability
Arbitrary geometric complexity
Multi-block domain variable transfer
Non-
conforming interface
Conforming interface
Linear (patch test)
Trigometric MMS

## Slide 7: Fluids/PMR Coupling
T, m, SRTE
Participating
Media
Radiation
n(n+2) DOF/node
VOLUME
Turbulent
Fluid Mechanics,
Combustion
15 dof/node
PMR
Fluids
Deflected reacting jet
Pool fire

## Slide 8: Fluids/PMR Coupling Equations
Favre-averaged static enthalpy equation:
Steady, non-scattering Radiative Transport Equation
Scalar Flux,
Divergence of radiative flux,
Quadrature

## Slide 9: PMR/Thermal Coupling
Irradiation
Temperature
Participating
Media
Radiation
n(n+2) DOF/node
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
1 DOF/node
+ chemistry
Thermal
PMR
ro, To = 0.1 m, 600K
r2, T2 = 0.075 m, 599.291K
ri, Ti = 0.03 m, 300K
r1, T1 = 0.05 m, 302.834K
PMR:Conduction through concentric spheres
O(1.8) with faceting,
O(2) without

## Slide 10: PMR/Thermal Coupling Equations
Steady, non-scattering Radiative Transport Equation
Irradiation (incoming),
Grey, diffuse boundary condition (given transmissivity, t, emissivity e, and reflectivity, r
With boundary condition,

## Slide 11: Stability of Operator Split CHT Approaches
Compute amplification factor: Tn+1 = l Tn Require:
CHT via flux transfer:
  Unstable for certain Dt and material property ratios
CHT via convection coefficient:
  Unconditionally stable, however, Dt error
Simplified 1D geometry with 2 nodes for stability analysis of CHT
Tspec
inflow
outflow
Convection Coef/Temp .
Temperature
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
1 DOF/node
+ chemistry
Turbulent
Fluid Mechanics,
Combustion
15 dof/node
Thermal
Fluids

## Slide 12: Conjugate Heat Transfer Coupling: In Practice
Using the control volume finite element method (CVFEM) – a Petrov-Galerkin approach
Using a Lagrange polynomial, and definition of element coefficients, interpolation is given by,
While gradients in temperature can be written as,
Thermal
Fluid
Dx
)
1F
2
“on the wall”, T1 terms collect to h
“off the wall”, T2 terms collect to Too
e
1A

## Slide 13: Conjugate Heat Transfer Coupling: Mathematical Construct
Given the definitions of the shape function derivatives on this simple 1D example,
Notes:
Regardless of flow physics, the heat transfer coefficient is always a function of the first mesh spacing
For high convective loads, this approach may not maximize stability of the Aria solve
However, we can arbitrarily increase h and modify Too consistently to achieve a larger diagonal dominance at the Aria system
We can also allow for h to be based on a physical bulk temperature, e.g., Tuser
Mandate: Modify the reference temperature and convection coefficient that thermal solution uses to ensure a consistent flux transfer between the CHT interface

## Slide 14: Conjugate Heat Transfer Coupling: Example
Flow past heated cylinder, Re = 1200
Water, Tcyl = 300C
Former analysis shows h = 5000 W/(m2 K) – fixed while user-based approach would provide ~2000 W/(m2 K)
Correlation provides h = 1500 W/(m2 K)
Modified post-processing based on inflow temperature
In this case, using a smaller h would reduce thermal solve’s diagonal dominance, however, would resonate with a typical ChemEngr or MechEngr
lhs += Int w h (T – Too) dA

## Slide 15: Other Linearization Procedures
PMR and heat conduction radiative boundary condition:
PMR and fluids coupling, linearized divergence of the radiative flux,
In practice, such procedures enhance stability for the multi-physics coupling
In the case of Fluids/CHT, one could possibly monolithically couple the systems
In the case of Fluids/PMR, monolithic coupling is not practical as the intensity system is ~ N2, where N is generally O(8)

## Slide 16: Why not simply monolithic CHT?
In some cases, the thermal response is extremely complex, e.g., includes enclosure radiation, thermal resistance, multiple interior fluids, etc.
For such complex cases, it may be best to operator split
However, if the thermal response is simple, then one might explore a multi-material non-conformal scheme, e.g., Domino, JCP, 2018
Non-conformal MMS
Other monolithic opportunities exist

## Slide 17: Multiphysics Coupling: Conclusions
Multiphysics applications are abundant in engineering applications
Turbulent, reacting flow with PMR and CHT requires a wide range of length and time scale resolution
Monolithic approaches are ideal from a splitting perspective, however, can be prohibitively expensive when considering systems such as PMR
Linearization can augment time step stability and should be exploited when possible

## Slide 18: Multiphysics Coupling: Conclusions
Multiphysics applications are abundant in engineering applications
Turbulent, reacting flow with PMR and CHT requires a wide range of length and time scale resolution
Monolithic approaches are ideal from a splitting perspective, however, can be prohibitively expensive when considering systems such as PMR
Linearization can augment time step stability and should be exploited when possible
Multiphysics Application
Operator split
Stability
Accuracy
Data transfer
Build system
Time-scale disparity
Monolithic
Efficient solvers
Flexible code design
Non-conformal interfaces
Time-scale disparity