## Slide 1
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4619 PE
Stanford ME469: Nalu Overview

## Slide 2: Nalu Overview: Outline
Nalu Technology Origination: ASC
Beyond the 32-bit Limit
Supported Physics
Supported Numerics
Low- and High-order
Moving Mesh (Sliding and Overset)
Multiphysics:
  Fluid Structure Interaction
  Conjugate Heat Transfer (CHT)
  Participating Media Radiation
Examples
Conclusion

## Slide 3: Core Technology Provided to Nalu Origination: Advanced Simulation and Computing Sierra/Fuego
Use-case characterized by a highly sooting, turbulent, reacting flow with Participating Media Radiation (PMR), Conjugate Heat Transfer (CHT), and propellant multi-physics coupling
Complex geometry has driven a generalized, hybrid unstructured discretization approach supporting Hex8, Tet4, Wedge6, and Pyramid5 elements in addition to arbitrary promotion of Hex8 to Hex27, Hex64, etc.

## Slide 4: Goal: Beyond 32-bit Computing
Circa 2013, many scientific production codes were limited to 32-bit
Therefore, maximum simulation size for entities, e.g., node, edge, face, element, etc., was ~2.2 billion
Next Generation Platforms were advocated to overcome poor MPI scaling and power needs to support Exascale computing (1018 floating point operations/second)
  Platform architectures, at that point, were not not yet known (still evolving)
( )
Sierra Toolkit/Trilinos (open-source)
MPI+X parallelism
Support for new architectures
+ ASC IC
Investments

## Slide 5: Developed Open-Source BSD-clause 3 Distribution Policy
Philosophy: Open-source collaborations
https://github.com/NaluCFD

## Slide 6: Supported Physics: DNS and LES (even RANS)

## Slide 7: A Note on High Performance Computing
Sandia is committed to High Performance Computing (HPC) to support is science and engineering objectives: Exercised herein
O(6) billion wind energy application
O(2) billion DNS impinging jet
O(200) million multi-physics fire

## Slide 8: High Performance Computing: Working in Parallel
Late Roman Timeline 250 AD - 300 AD
250 AD: The Goths invade Anatolia (AKA, Asia Minor), in sea-borne raids they plunder Nikopolis
Trinity open-science time, Domino and Barone, 2016 SAND2016-4085C to elucidate stall cells
O(6) billion element wind energy application (high-Re flow past thick blade in high AoA
O(128,0000) core run for ~one week ~1800 year simulation using computing resources available 10-years ago: Complete in roughly 29 years!

## Slide 9: Change of Philosophy: Former Approach
Verify on nice Hexahedral-based elements
Validate on perfect meshes on a variety of canonical flows
Ret 395 plane-channel (Jofre, Domino, Iaccarino, Flow, Turb. & Comb., 2018)
Variable-density low-Mach MMS (Domino, CTRSP, 2016)

## Slide 10: Paradigm Shift: Verify and Deploy High-Quality Unstructured Numerical Methods
Verify on awful hybrid mesh element quality
Validate on non-ideal meshes on a variety of canonical flows
P1/P1
P1/P2
P2/P2
P2/P1
Domino, J. Comp. Phys. Flow, 2018

## Slide 11: Confidence Established for Atypical Element Topos
Verification
Validation

## Slide 12: Nalu History
A time-history of the Nalu code base:
By CFD standards, this is a relatively new code base
Sierra/Nalu
SNL License
Github
Nalu
Open-source
BSD License (2014)
Active
academic partners
Github
Nalu-Wind
ECP ExaWind (2018)
Open-source: SNL, NREL, ORNL, UT joint copyright

## Slide 13: Supported Discretizations: CVFEM/FEM/EBVC
The core discretization used in the low Mach code base has been the Control Volume Finite Element Method, CVFEM
Finite Element Method and Edge-based Vertex-Centered, EBVC, are also supported

## Slide 14: Scientific Research Platform to Evaluate Higher-Order Methods on Next Generation Platforms
As the cost of parallel assembly increases, should we strive to perform more local work? Higher-order achieves this design-point (at the cost of a larger memory footprint)
Spectral convergence
Dual-volume
for promoted quad4
Flow-past rotating cube
Re~4000, RPM~3200
Same node count,
P=1 (top) P=2 (bot)

## Slide 15: Several Multi-physics Flow Examples From Nalu
Impinging Jet DNS
Cylinder in cross flow
Whirling behavior
Helium plume (low-/high-order)
Heated backstep

## Slide 16: Evolution of a Mindset….. Modeling Whirling-like Flow
  Idealized chamber in which swirl is provided by selective wall placement in the experimental design
  Gap varied between 10, 20, and 40 cm
  Objective: Can the onset of swirl be predicted? What is the strength?
Volume rendered mixture fraction
SAND2019-7052 C
Notes: Fire whirls are complex phenomena that we are just understanding and, only recently, can model.
This is an example where we have engineered slots in walls that inspire vortical flow in the inner chamber. The plume accelerates upward and, therefore, entrains fluid. The slots provide a large-scale clockwise rotation.

## Slide 17: Unique Complex Geometry Use-Cases
Low-dissipation methods with suitable nonlinear stabilization operators using sliding and overset technologies to aid modeling effort and/or meshing
Objective: Design-order established/verified implementations on generalized, unstructured, hybrid meshes
Vertical Axis Wind Turbine
(VAWT)
Horizontal Axis Wind Turbine
(HAWT)

## Slide 18: Nalu Abstractions: Polymorphic and Input File-Driven
Domain
Time Integration
Realm B
Realm A
1 to many
boundary
algorithms
1 to many
Interior
algorithms
Transfer
1 to many
boundary
algorithms
1 to many
Interior
algorithms
Nonlinear Coupling
Operator-split multi-physics
Conjugate heat transfer coupling
Fluids Realm
Heat Conduction Realm
Realm specifications define the physics and desired boundary conditions
Pre-defined EquationSystems (segregated or monolithic)

## Slide 19: 30K View: Anatomy of a Nalu Input File:YAML-based
Simulation:
linear_solvers:
transfers:
realms:
- name: realm_heatCond
boundary_conditions:
- wall_boundary_condition: bc_exposed
solution_options:
initial_conditions:
material_properties:
equation_systems:
systems:
- HeatConduction:
output:
restart:
- name: realm_fluids
TimeIntegrators:
Specification of sparse Trilinos-based precond/solver
Data transfer for multi-physics coupling
Physics definitions
Time integration, e.g., BE, BDF2
YAML enforces strict spacing and ordering
https://www.democraticunderground.com/10021540110

## Slide 20: High-Level Elements of an Input File
systems:
- LowMachEOM:
name: myLowMach
- MixtureFraction:
name: myZ
initial_conditions:
- constant: ic_1
target_name: [block_1, …]
value:
pressure: 0
velocity: [0.5,0.0]
mixture_fraction: 0.0
material_properties:
target_name: block_1
specifications:
- name: density
type: constant
value: 1.0
- name: viscosity
type: constant
value: 1.8e-5
boundary_conditions:
- inflow_boundary_condition: bc_left_inflow
- wall_boundary_condition: bc_front_wall
- open_boundary_condition: bc_right_open
- symmetry_boundary_condition: bc_top
- nonconformal_boundary_condition: bc_nc
- inflow_boundary_condition: bc_left
target_name: surface_1
inflow_user_data:
velocity: [0.5,0.0,0.0]
mixture_fraction: 0.0
material_properties:
target_name: block_1
specifications:
- name: density
type: ideal_gas
- name: viscosity
type: polynomial
coefficient_declaration:
- wall_boundary_condition: bc_back
target_name: surface_7
wall_user_data:
user_function_name:
velocity: wind_energy
user_function_string_parameters:
velocity: [mmTop_ss7]
mixture_fraction: 1.0

## Slide 21: A Note on Parallel Decomposition
As noted, decomposing the mesh into small subsets and operating on these subsets in parallel provides a methodology for increased simulation time
Colored by block ID
Colored by core count (= 1) One mpi rank. 16 MPI ranks = 16x faster (hopefully)

## Slide 22: How to Run in Parallel: Mesh Decomposition
Given a mesh, mesh.g and myInputFile.i, if one desires to run on, e.g., 16 core case:
Use pre-processing “decomposition” tools (Trilinos/install/bin)
In-situ
- name: realmFluids
mesh: mesh/myMesh.g
automatic_decomposition_type: rcb
myMesh.g
- name: realmFluids
mesh: mesh/myMesh.g
automatic_decomposition_type: rcb
>/path/to/decomp –j {np} {meshName}
>mesh.g.16.00, mesh.g.16.01, .., mesh.g.16.15
>results.e.16.00, results.e.16.01, .., results.e.16.15
>input.log
2:
1:
>mpirun --np 16 /naluPath/naluX -i input.i &

## Slide 23: A Note on Divergence
Whether by design or poor code usage, solution results from CFD analysis for complex applications may diverge. How do I know?
Non-finite residuals, i.e., not-a-number:“nan” (either linear or non-linear),
  const double norm = 0.0;
  const double flux = rho*u*A/norm;
Simulation runs, however, results look very wrong
Typical causes?
Bad initial condition that drives nonlinear solution to diverge
Too large of an initial time step
Poor stabilization, numerical parameters, etc.
Poor time integration
Ph.D. from ICME explaining why…
EBVC flow-past 2D cylinder
Top: +NOC
Bottom se: -NOC

## Slide 24: Test Case Input Files
  All input files are part of the Nalu regression test suite: Nalu/reg_test/test_files
  Mesh files are found under: Nalu/reg_test/mesh
    Formally, /mesh is a git submodule
  Test Cases Highlighted:
  Nalu/reg_tests/test_files/dgNonConformalThreeBlade
  Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
  Homework #1:
    https://github.com/spdomin/Present/tree/master/standformMe469/hwOne
Feel free to run any case that you feel looks interesting to you!
Note that the regression test suite is (mostly) focused on providing code coverage and may not represent “sane” physics-based choices
Resource: https://nalu.readthedocs.io/en/latest/source/theory/index.html

## Slide 25: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Physics
  Flow past rotating square blades (Re = 10,000)
Models
  Newtonian fluid (air) with constant properties
Boundary Conditions
  Inflow, open, symmetry, DG/CVFEM interface
>mpirun --np 4 /naluPath/naluX -i dgNonConformalThreeBlade.i &
Domino, JCP, 2018

## Slide 26: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Time Step Count: 7 Current Time: 0.0127268
dtN: 0.00266002 dtNm1: 0.00231306 gammas: 1.53488 -2.15 0.615116
Max Courant: 1.54421 Max Reynolds: 236.792 (realm_1)
Realm Nonlinear Iteration: 1/1
realm_1::advance_time_step()
NLI Name Linear Iter Linear Res NLinear Res Scaled NLR
--- ---- ----------- ---------- ----------- ----------
1/2 Equation System Iteration
1/1 myLowMach
MomentumEQS 4 1.27653e-07 0.000173716 1
ContinuityEQS 9 5.17721e-06 0.00618278 1
PNGradPEQS 19 4.2818e-09 2.78318e-06 1
PNGradUEQS 20 9.70201e-09 5.20951e-06 1
1/1 myZ
MixtureFractionEQS 5 1.31346e-09 6.84724e-06 1
PNGradZEQS 5 6.33586e-09 3.66957e-06 1
2/2 Equation System Iteration
1/1 myLowMach
MomentumEQS 5 8.33682e-10 2.23818e-06 0.0128842
Mass Balance Review:
Density accumulation: 0
Integrated inflow: -0.375
Integrated open: 0.3749998354138842
Total mass closure: -1.64586e-07
Mean System Norm: 0.0002458198407611864 7 0.0127268
gi for BDF2
UDt/Dx
r U L / m
nonlinear
iterations
equations
Review

## Slide 27: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Physics
  Uniformly emitting/absorbing participating media radiation (PMR) conjugate heat transfer (CHT) with buoyancy
Models
  Newtonian fluid (air): ideal gas
Boundary Conditions
  Wall, periodic
>mpirun --np 8 /naluPath/naluX -i fluidsPmrChtPeriodic.i &
Stark#, cond/rad
Sk = l m / s Ti3 ~ 0.4
Rayleigh#, tThermalDiff/ tConv
Ra = g b (Ti – To ) L / Pr a2 ~ 2e6

## Slide 28: Nalu/reg_tests/test_files/fluidsPmrChtPeriodic
Monolithic, i.e., fully coupled, approaches are intractable due to the size of (u, v, w, p, h, hr, Z, Ik T)T
Stable and accurate operator split methods are, therefore, sought
  See Domino et al., AIAA, 2007
Temperature
Irradiation
Participating
Media
Radiation DOM
STK
Transfer
VOLUME
SURFACE
Δ
۰qr
Temperature, mg
RTE Src
Linearized
Temperature
Convection Coef.
Reference Temp
SURFACE
Conduction
Heat Transfer,
Enclosure Radiation
Turbulent
Fluid Mechanics,
Combustion

## Slide 29: Laminar Pipe Flow: Specified Pressure Drop for Ret= 10
Physics
  Laminar pipe flow (specified pressure drop)
Models
  Newtonian fluid (air): ideal gas
Boundary Conditions
  Wall, open (pressure specified)
Location: https://github.com/spdomin/Present/tree/master/stanfordMe469/hw/one
Specifications:
  Ret = 10
  Pipe diameter, D = 0.01 m
  Pipe Length, L = 0.2 m
  r = TBD
  m = TBD
  dp/dz = TBD
  Uc = TBD

## Slide 30: Break-out Example Using Paraview
Live in-class demo

## Slide 31: Nalu Overview: Conclusion
Nalu’s technology has its roots in the ASC Sierra/Fuego effort
Multi-physics capabilities are in development
Research platform for high-order low-Mach methods
Open-source collaboration model
Multi-physics by design (operator split)
Funded through ASC, ECP, A2e, ASCR, and LDRD
Elements of an input file
  Solvers, mesh, equations, material models, boundary conditions, etc.
The need for parallel computing
Examples
  Fixed rotation for three blades
  Thermal/PMR/Fluids
Paraview to visualize