## Slide 1
Stefan P. Domino
Computational Thermal and Fluid Mechanics
Sandia National Laboratories SAND2018-4536 PE
Stanford ME469: High Performance Computing for CFD

## Slide 2: High Performance Computing for CFD: Outline
Overview of Time and Length Scales
  Fire
  Wind
Conceptual Parallel Computing Model
Types of Scaling: Strong and Weak
Examples of Scaling
Next Generation Platform Exascale Drivers
Conclusions

## Slide 3: Disparity in Time and Length Scales, Fire
Engineering Scale of Interest
Convective Transport
Heat Transfer in Weapon
Flames
Chemical Kinetics
Molecular Transport
Diffusive Transport
Soot
Products
Fuel Distribution
Convection
Molecular Radiation
Soot Radiation
Soot Growth
10-10
102
10-8
10-6
10-4
10-2
100
Length Scale, meters
Time Scale, seconds
10-12
10-9
10-6
10-3
100
103

## Slide 4: Disparity in Time and Length Scales, Wind
Engineering Scale of Interest
Convective Transport
104
10-6
10-4
10-2
100
102
Length Scale, meters
Time Scale, seconds
10-6
10-3
100
103
Knight & Carver
Severe Leading Edge Erosion
Sound propagation (turbulent atmosphere and complex domains)

## Slide 5: Conceptual Scaling Exercise
Goal: Paint a house in one day
  My House: 1000 sq ft
  WH: 60,000 sq ft
One person would paint my house in two days (!!)
The white house will require one person 120 days (!!)
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend

## Slide 6: Single House, More People (each person with reduced load)
Goal: Paint a house in one day
  My House: 1000 sq ft
  WH: 60,000 sq ft
+
= One day
+
= Faster Completion; Half day (each person 250 sq ft)
+
+
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend

## Slide 7: Single House, More People (with shared load)
( )
Goal: Paint a house in one day
  My House: 1000 sq ft
  WH: 60,000 sq ft
+
= 60 days
+
= 1 day
60x
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend
Time to completion is one day. Everyone
involved provided 500 sq ft

## Slide 8: Single House, More People (with impediments)
( )
Impediments:
  Peter’s team, who played basketball last night, have some injuries
  Limited paint brushes…
  Plenty of paint, poor loading capacity
  No coherent plan of attack
+
= 60 days
+
>> 1 day
60x
= 500 sq ft/day
= 500 sq ft/day
Painting Rate Legend
~ 250 sq ft/day
+
n
…

## Slide 9: Types of Scaling
Strong Scaling: How the solution time varies with increased computational resources (cores, threads, GPU/Warps) on a fixed-size problem
  User Y has a mesh that is 1 billion elements and would like to minimize the time it takes to complete a simulation; the larger the resource, the faster the turn-around
Weak Scaling: How the solution time varies with increased problem size on a fixed computational resource load (cores, threads, GPU/Warps)
  User Y is conducting a validation study that includes three mesh resolutions, which were obtained by uniform mesh refinement, and would like to increase the computational resource appropriately for each subsequently refined mesh
Strong Scaling
Weak Scaling

## Slide 10: Types of Scaling
Strong Scaling: How the solution time varies with increased computational resources (cores, threads, GPU/Warps) on a fixed-size problem
  User Y has a mesh that is 1 billion elements and would like to minimize the time it takes to complete a simulation; the larger the resource, the faster the turn-around
Weak Scaling: How the solution time varies with increased problem size on a fixed computational resource load (cores, threads, GPU/Warps)
  User Y is conducting a validation study that includes three mesh resolutions, which were obtained by uniform mesh refinement, and would like to increase the computational resource appropriately for each subsequently refined mesh
Strong Scaling
Weak Scaling
~4,000 elem/core
~8,000 elem/core
General Implicit Rules:
1e6 elem/node
~25k elem/core

## Slide 11: Challenges Associated with Scaling
Consider a communication-intensive code procedure: Algebraic Multigrid (AMG) preconditioner setup
Like verification, the product of a first-time scaling study at a new production scale is generally met with work!
+
+
+
+
+
+
+

## Slide 12: Computing Performance: Through the Years
Mainframes
60’s to 70’s
Vector
Supercomputers
70’s to early 90’s
Technology disruptions require a significant increase in complexity of our codes
MPP w/ Advanced Architecture nodes: Multilevel, heterogeneous, energy and memory constrained
ROOM  MACHINE  CABINET  CHIP
COMPLEXITY
Massively parallel processor (MPP) systems with simple nodes
1990’s to 2010
HPC is facing a new disruption in technology
Slides courtesy of Mike Glass, Jim Ang, Rob Hoekstra, Si Hammond, Ron Brightwell, and Stephen Olivier.

## Slide 13: Drive Towards Next Generation Platforms
Chart: Memory / Core
| Purple ('05) | Red Storm ('05) | Dawn ('09) | Cielo ('10) | TLCC2 ('11) | Sequoia ('12) | Future (est.)
Mem/core | 4 | 2 | 1 | 2 | 2 | 1 | 0.2
B:F | 1.6 | 0.44 | 1 | 0.86 | 0.83 | 0.22 | 0.03
Dramatic increase in on-node parallelism and reduction in relative data movement is counter to our current code performance
Sequoia Parallelism = 5M
Cielo Parallelism = 100K
RATIO = 50
Power constraints are driving the rapid increase in on-node parallelism.
However, per core memory bandwidth is decreasing making it extremely difficult to fully utilize additional cores
Slides courtesy of Mike Glass, Jim Ang, Rob Hoekstra, Si Hammond, Ron Brightwell, and Stephen Olivier.
https://www.hpcwire.com/2015/11/20/top500/

## Slide 14: Nalu/reg_tests/test_files/dgNonConformalThreeBlade
Recall the first task assigned, dgNonConformalThreeBlade inclued the following line command within the input file:
Colored by block ID
- name: realm_1
automatic_decomposition_type: [type]
Colored by core count (= 1)

## Slide 15: High Performance Computing for CFD: Conclusions
Several fluids applications found in the low-Mach application space require HPC
Strong and weak scaling are of interest in engineering analysis
Communication bottlenecks can affect scaling
From a user-perspective, scaling is critical to efficiently deploying production simulation results
Path towards NGP will require disruptive technology with significant code investments